## Slide 1: Guide to Networking Essentials 7th Edition
Topic 01
Network Topologies and Technologies
Notes: Network+ Guide to Networks 7th Edition
Chapter 3
Network Topologies and Technologies

## Slide 2: Objectives
Describe the primary physical networking topologies in common use
Describe the primary logical networking topologies in common use
Describe major LAN networking technologies
Compare Wi-Fi standards
Notes: Objectives
Describe the primary physical networking topologies in common use
Describe the primary logical networking topologies in common use
Describe major LAN networking technologies
Compare Wi-Fi standards

## Slide 3: Physical Topologies
Topology: describes the lay of the land (configuration)
A network topology describes how a network is physically laid out and how signals travel from one device to another
The physical layout of the devices and cables doesn’t describe how signals travel from one device to another
  Hence network topologies are categorized into physical and logical topologies
Notes: Physical Topologies
Topology: describes the lay of the land
A network topology describes how a network is physically laid out and how signals travel from one device to another
The physical layout of the devices and cables doesn’t describe how signals travel from one device to another
  Network topologies are categorized into physical and logical topologies

## Slide 4: Physical Topologies
The arrangement of cabling and how cables connect one device to another in a network is considered the network’s physical topology
The path data travels between computers on a network is considered the network’s logical topology
All network designs today are based on these basic physical topologies: bus, star, ring, meshed and point-to-point
Notes: Physical Topologies
The arrangement of cabling and how cables connect one device to another in a network is considered the network’s physical topology
The path data travels between computers on a network is considered the network’s logical topology
All network designs today are based on these basic physical topologies: bus, star, ring, and point-to-point

## Slide 5: Physical Bus Topology
Physical bus topology is defined as a continuous length of cable connecting one computer to another in daisy-chain fashion
  The simplest and at one time the most common method for connecting computers
Weaknesses
  There’s a limit of 30 computers per cable segment
  The maximum total length of cabling is 185 meters
  Both ends of the bus must be terminated (terminator at the both ends of the cable)
  Any break in the bus brings down the entire network
Notes: Physical Bus Topology
Physical bus topology is defined as a continuous length of cable connecting one computer to another in daisy-chain fashion
  The simplest and at one time the most common method for connecting computers
Weaknesses
  There’s a limit of 30 computers per cable segment
  The maximum total length of cabling is 185 meters (can be extended by adding repeaters between segments)
  Both ends of the bus must be terminated (otherwise signal will echo back into the cable and cause collision, bringing down the network)
  Any break in the bus brings down the entire network
  5/4/3 rules:
  5 segments connected by 4 repeaters, only 3 segments can have computers/devices.

## Slide 6: Physical Bus Topology
Weaknesses (cont’d)
  Adding or removing a machine brings down the entire network temporarily
  Technologies using this topology are limited to 10 Mbps half-duplex communication since they use coaxial cabling
Due to the limitations, this topology is no longer a practical choice and technology has moved past this obsolete method of connecting computers
Notes: Physical Bus Topology
Weaknesses (cont’d)
  Adding or removing a machine brings down the entire network temporarily
  Technologies using this topology are limited to 10 Mbps half-duplex communication since they use coaxial cabling
Due to the limitations, this topology is no longer a practical choice and technology has moved past this obsolete method of connecting computers

## Slide 7: Physical Bus Topology
Notes: Physical Bus Topology

## Slide 8: How Data Travels in a Physical Bus
Electrical pulses (signals) travel the cable’s length in all directions
Signal travel across the medium and from device to device is called signal propagation
Signal continues until it weakens or is absorbed by terminator ( at the end of both ends of the cable )
  A terminator is an electrical component called a resistor that absorbs the signal instead of allowing it to bounce back up the wire
If not terminated, signal bounces or is “reflected” at end of medium (BAD)
  Signal bounce is the term used when electricity bounces off the end of a cable and back in the other direction (causes echo)
Notes: How Data Travels in a Physical Bus
Electrical pulses (signals) travel the cable’s length in all directions
Signal travel across the medium and from device to device is called signal propagation
Signal continues until it weakens or is absorbed by terminator
  A terminator is an electrical component called a resistor that absorbs the signal instead of allowing it to bounce back up the wire
If not terminated, signal bounces or is “reflected” at end of medium
  Signal bounce is the term used when electricity bounces off the end of a cable and back in the other direction

## Slide 9: Data signals travel to both ends of the bus

## Slide 10: Physical Bus Limitations
Only 30 computers can be daisy-chained together
  Before signal becomes too weak to be passed along to another computer
As an electrical signal encounters each workstation along a daisy-chain
  Some of its strength is absorbed by both the cabling and the connectors until the signal is too weak for a NIC to interpret
For the same reason, total length of cabling is limited to 185 meters
Notes: Physical Bus Limitations
Only 30 computers can be daisy-chained together
  Before signal becomes too weak to be passed along to another computer
As an electrical signal encounters each workstation along a daisy-chain
  Some of its strength is absorbed by both the cabling and the connectors until the signal is too weak for a NIC to interpret
For the same reason, total length of cabling is limited to 185 meters

## Slide 11: Physical Star Topology
Uses a central device (hub or switch) to connect computers
Advantages:
  Much faster technologies than a bus
  Centralized monitoring and management of network traffic are possible
  Easier network upgrades
Detecting errors ( checksum )
Notes: Physical Star Topology
Uses a central device (hub or switch) to connect computers
Advantages:
  Much faster technologies than a bus
  Centralized monitoring and management of network traffic are possible
  Easier network upgrades

## Slide 12: Physical Star Topology
Notes: Physical Star Topology

## Slide 13: Physical Star Topology
Using a central device allows for monitoring and managing a network
  Hubs and switches can include software that collects statistics about network traffic patterns and detect errors
  As long as cabling and NICs support it, a star network can be easily updated by replacing the central device (for higher speed if needed e.g. 100Mbps to 1Gbps)
When the number of workstations you need exceed the number of ports on a central device you simply add another central device ( extended star )
Notes: Physical Star Topology
Using a central device allows for monitoring and managing a network
  Hubs and switches can include software that collects statistics about network traffic patterns and detect errors
  As long as cabling and NICs support it, a star network can be easily updated by replacing the central device
When the number of workstations you need exceed the number of ports on a central device you simply add another central device

## Slide 14: Extended Star
When several hubs or switches must be connected, usually one device is used as the central connecting point, forming an extended star topology
Notes: Extended Star
When several hubs or switches must be connected, usually one device is used as the central connecting point, forming an extended star topology

## Slide 15: Extended Star
Most widely used in networks containing more than just a few computers
A central device (usually a switch) sits in the middle and instead of attached computers, other switches or hubs are connected to the central switch’s ports
  Computers and peripherals are then attached to these switches or hubs forming additional stars
Sometimes referred to as a “hierarchical star”
Notes: Extended Star
Most widely used in networks containing more than just a few computers
A central device (usually a switch) sits in the middle and instead of attached computers, other switches or hubs are connected to the central switch’s ports
  Computers and peripherals are then attached to these switches or hubs forming additional stars
Sometimes referred to as a “hierarchical star”

## Slide 16: Hierarchical Star

## Slide 17: How Data Travels in a Physical Star
Depends on the type of central device
Central device determines ‘logical’ topology
  Logical topology is discussed later in the chapter
  For now: hub = logical bus; switch = logical switching; MAU = logical ring
Notes: How Data Travels in a Physical Star
Depends on the type of central device
Central device determines ‘logical’ topology
  Logical topology is discussed later in the chapter
  For now: hub = logical bus; switch = logical switching; MAU = logical ring

## Slide 18: Physical Star Disadvantages
There are many advantages of a physical star
There is one disadvantage
  The central device represents a single point of failure
  If the hub or switch fails or someone kicks the power cord out of the outlet, the entire network goes down
  Having a spare on hand is a good idea
Notes: Physical Star Disadvantages
There are many advantages of a physical star
There is one disadvantage
  The central device represents a single point of failure
  If the hub or switch fails or someone kicks the power cord out of the outlet, the entire network goes down
  Having a spare on hand is a good idea

## Slide 19: Physical Ring Topology
A physical ring topology is like a bus
  Devices are daisy-chained one to another
  Instead of terminating each end, the cabling is brought around from the last device back to the first device to form a ring
Most widely used to connect LANs with a technology called Fiber Distributed Data Interface (FDDI)
FDDI was most often used as a network backbone, which is cabling used to communicate between LANs or between hubs and switches
Notes: Physical Ring Topology
A physical ring topology is like a bus
  Devices are daisy-chained one to another
  Instead of terminating each end, the cabling is brought around from the last device back to the first device to form a ring
Most widely used to connect LANs with a technology called Fiber Distributed Data Interface (FDDI)
FDDI was most often used as a network backbone, which is cabling used to communicate between LANs or between hubs and switches

## Slide 20
FDDI is used as a high speed backbone to connect servers, switches (which connects LANs) and terminal concentrators (which connects terminals)
2 fibre optic cables for higher speed + backup if one fails

## Slide 21: Physical Ring Topology
Data travels in one direction
If any station in the ring fails, data can no longer be passed along
FDDI uses dual ring
  Data travels in both directions
  One ring failure doesn’t break network
  Operates using fiber-optic cable at 100 Mbps
  Extended star topologies with Gigabit Ethernet has largely replaced FDDI
Notes: Physical Ring Topology
Data travels in one direction
If any station in the ring fails, data can no longer be passed along
FDDI uses dual ring
  Data travels in both directions
  One ring failure doesn’t break network
  Operates using fiber-optic cable at 100 Mbps
  Extended star topologies with Gigabit Ethernet has largely replaced FDDI

## Slide 22: Physical Ring Topology
Notes: Physical Ring Topology

## Slide 23: Point-to-Point Topology
Direct link between two devices
Mostly used in WANs (connecting say HQ in New York to branch office in Tokyo)
Wireless bridge (connect 2 LANs separated by highway, river or railway tracks)
Used to connect two computers
Notes: Point-to-Point Topology
Direct link between two devices
Mostly used in WANs
Wireless bridge
Used to connect two computers

## Slide 24: Point-to-Multipoint Topology
Point-to-multipoint (PMP) topology – a central device communicates with two or more other devices
  All communication goes through the central device
Often used in WANs where a main office has connections to several branch offices via a router
  A single connection is made from the router to a switching device that directs traffic to the correct branch office
Also used in wireless network arrangements
(wi- max)
Notes: Point-to-Multipoint Topology
Point-to-multipoint (PMP) topology – a central device communicates with two or more other devices
  All communication goes through the central device
Often used in WANs where a main office has connections to several branch offices via a router
  A single connection is made from the router to a switching device that directs traffic to the correct branch office
Also used in wireless network arrangements

## Slide 25: Point-to-Multipoint Topology
Notes: Point-to-Multipoint Topology

## Slide 26: Mesh Topology
Connects each device to every other device in a network
  Multiple point-to-point connections for the purposes of redundancy and fault tolerance
Purpose of creating a mesh topology is to ensure that if one or more connections fail, there’s another path for reaching all devices on the network
Expensive due to multiple interfaces and cabling
Found in large WANs and internetworks
Notes: Mesh Topology
Connects each device to every other device in a network
  Multiple point-to-point connections for the purposes of redundancy and fault tolerance
Purpose of creating a mesh topology is to ensure that if one or more connections fail, there’s another path for reaching all devices on the network
Expensive due to multiple interfaces and cabling
Found in large WANs and internetworks

## Slide 27: Mesh Topology
Figure 3-7 Switches in each building are connected in a full mesh topology
Notes: Mesh Topology
Fully meshed networks require n (n – 1) /2 connectons,

## Slide 28: Logical Topologies
Describes how data travels from computer to computer
Sometimes same as physical topology
  In a physical bus and physical ring, the logical topology mimics the physical arrangement of cables
  Physical Bus and Logical Bus
  Physical Ring and Logical Ring
  For physical star, electronics in central device determine logical topology
Notes: Logical Topologies
Describes how data travels from computer to computer
Sometimes same as physical topology
  In a physical bus and physical ring, the logical topology mimics the physical arrangement of cables
  For physical star, electronics in central device determine logical topology

## Slide 29: Logical Topologies
Notes: Logical Topologies

## Slide 30: Logical Topologies
A logical ring using a physical star implements the ring inside the central device’s electronics, which is a MAU ( multistation access unit) in the token ring technology
Notes: Logical Topologies
A logical ring using a physical star implements the ring inside the central device’s electronics, which is a MAU in the token ring technology

## Slide 31: Logical Topologies
In a switched topology, there is always an electrical connection between the computer and the switch
  But when no data is being transferred there is no logical connection or circuit between the devices
Notes: Logical Topologies
In a switched topology, there is always an electrical connection between the computer and the switch
  But when no data is being transferred there is no logical connection or circuit between the devices

## Slide 32: Logical Topologies
Notes: Logical Topologies

## Slide 33: Layers ( People don’t need to see president America )
Application
Presentation Session
Transport Network Data Physical

## Slide 34: Network Technologies
Network technology is the method a NIC uses to access the medium and send data frames
Other terms:
  Network interface layer technologies
  Network architectures
  Data link layer technologies
Basically, it is whether your network uses Ethernet, 802.11 wireless, token ring, or some combination of these to move data from device to device in your network
Notes: Network Technologies
Network technology is the method a NIC uses to access the medium and send data frames
Other terms:
  Network interface layer technologies
  Network architectures
  Data link layer technologies
Basically, it is whether your network uses Ethernet, 802.11 wireless, token ring, or some combination of these to move data from device to device in your network

## Slide 35: Network Technologies
LAN examples include
  Ethernet
  802.11 wireless ( Wi-fi )
  Token Ring
WAN examples include
  Frame relay
  FDDI
  ATM ( Asynchronous transfer mode )
  Gigabit Ethernet ( Nowadays )
Network technology often defines frame format and media
Notes: Network Technologies
LAN examples include
  Ethernet
  802.11 wireless
  Token Ring
WAN examples include
  Frame relay
  FDDI
  ATM
Network technology often defines frame format and media

## Slide 36: Network Technologies and Media
Unshielded Twisted pair (UTP)
  Most common media type in LANs
  Consists of 4 pairs of copper wires
  each twisted together (Minimizes the EMI, electro magnetic interference)
  Comes in numbered categories
Fiber-optic cabling uses thin strands of glass to carry pulses of light long distances and at high data rates
Coaxial cable is obsolete as a LAN medium but it is used as the network medium for Internet access via cable modem
Notes: Network Technologies and Media
Unshielded Twisted pair (UTP)
  Most common media type in LANs
  Consists of 4 pairs of copper wires
  each twisted together
  Comes in numbered categories e.g. Cat 3,4,5,6 etc
Fiber-optic cabling uses thin strands of glass to carry pulses of light long distances and at high data rates
Coaxial cable is obsolete as a LAN medium but it is used as the network medium for Internet access via cable modem

## Slide 37: Categories of UTP Cables

## Slide 38: Baseband and Broadband Signaling
Network technologies can use media to transmit signals in two main ways
Baseband sends digital signals in which each bit of data is represented by a pulse of electricity or light
  Sent at a single fixed frequency and no other frames can be sent along with it (no more than 1 frame can be sent at the same time)
Broadband uses analog techniques to encode binary 1s and 0s across a continuous range of values
  Signals flow at a particular frequency and each frequency represents a channel of data (can have several transmissions occurring at the same time)
Notes: Baseband and Broadband Signaling
Network technologies can use media to transmit signals in two main ways
Baseband sends digital signals in which each bit of data is represented by a pulse of electricity or light
  Sent at a single fixed frequency and no other frames can be sent along with it
Broadband uses analog techniques to encode binary 1s and 0s across a continuous range of values
  Signals flow at a particular frequency and each frequency represents a channel of data.
  (can have several transmissions occurring at the same time – each on different frequency - channel)

## Slide 39: Ethernet Networks
Ethernet is the most popular LAN technology
  Easy to install and support with a low-cost factor
  It is baseband
Supports a broad range of speeds: 10 Mbps to 10 Gbps
Can operate in physical bus or physical star and logical bus or switched logical topology
Most NICs/hubs/switches can operate at multiple speeds: 10/100/1000
  Underlying technology is the same
Notes: Ethernet Networks
Ethernet is the most popular LAN technology
  Easy to install and support with a low cost factor
Supports a broad range of speeds: 10 Mbps to 10 Gbps
Can operate in physical bus or physical star and logical bus or switched logical topology
Most NICs/hubs/switches can operate at multiple speeds: 10/100/1000
  Underlying technology is the same

## Slide 40: Ethernet Addressing
Every station has a physical (MAC) address
Each MAC address has 48 bits expressed as 12 hexadecimal digits
Incoming frames must match NIC’s address or broadcast address (FF-FF-FF-FF-FF-FF). First 6 digits represent manufacturer
Once processed by NIC, incoming frames are sent to the network protocol for further processing
Notes: Ethernet Addressing
Every station has a physical (MAC) address
Each MAC address has 48 bits expressed as 12 hexadecimal digits
Incoming frames must match NIC’s address or broadcast address (FF-FF-FF-FF-FF-FF).
Once processed by NIC, incoming frames are sent to the network protocol for further processing

## Slide 41: Ethernet Frames
Four different formats or frame types –depending on the network protocol used to send the frame
Ethernet II frame type used by TCP/IP
  TCP/IP has become the dominant network protocol in LANs so supporting multiple frame types has become unnecessary
Frames must be between 64 and 1518 bytes
  Destination MAC
  Source MAC
  Type
  Data
  FCS ( Frame check sum )
Notes: Ethernet Frames
Four different formats or frame types –depending on the network protocol used to send the frame
Ethernet II frame type used by TCP/IP
  TCP/IP has become the dominant network protocol in LANs so supporting multiple frame types has become unnecessary
Frames must be between 64 and 1518 bytes
  Destination MAC
  Source MAC
  Type
  Data
  FCS

## Slide 42: Ethernet Media Access
Media access method: Rules governing how and when the medium can be accessed for transmission
Ethernet uses Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
  Carrier Sense: Listen before send – must hear silence
  Multiple Access: If two or more stations hear silence, multiple stations may transmit at the same time
  Collision Detection: If two or more stations transmit, a collision occurs and is detected by the NIC; all stations must retransmit
  Simulation 7 : CSMA/CD Ethernet
Notes: Ethernet Media Access
Media access method: Rules governing how and when the medium can be accessed for transmission
Ethernet uses Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
  Carrier Sense: Listen before send – must hear silence
  Multiple Access: If two or more stations hear silence, multiple stations may transmit at the same time
  Collision Detection: If two or more stations transmit, a collision occurs and is detected by the NIC; all stations must retransmit

## Slide 43: Collisions and Collision Domains
All devices interconnected by one or more hubs hear all signals generated by all other devices
The extent to which signals in an Ethernet bus topology network are propagated is called a collision domain
All devices in a collision domain are subject to the possibility that whenever a device sends a frame, a collision might occur
Notes: Collisions and Collision Domains
All devices interconnected by one or more hubs hear all signals generated by all other devices
The extent to which signals in an Ethernet bus topology network are propagated is called a collision domain
All devices in a collision domain are subject to the possibility that whenever a device sends a frame, a collision might occur

## Slide 44: Collisions and Collision Domains
Notes: Collisions and Collision Domains

## Slide 45: Ethernet Error Handling
Ethernet is a best-effort delivery system
  Like the post-office; you hope it gets there but there is no acknowledgement either way
  Network protocols and applications ensure delivery
  Only collisions are automatically retransmitted
Ethernet detects damaged frames
  The error-checking code in an frame’s trailer is called a Cyclic Redundancy Check (CRC)
  Uses CRC to determine that data is unchanged
  If a frame is detected as damaged, it is discarded with no notification
Notes: Ethernet Error Handling
Ethernet is a best-effort delivery system
  Like the post-office; you hope it gets there but there is no acknowledgement either way
  Network protocols and applications ensure delivery
  Only collisions are automatically retransmitted
Ethernet detects damaged frames
  The error-checking code in an frame’s trailer is called a Cyclic Redundancy Check (CRC)
  Uses CRC to determine that data is unchanged
  If a frame is detected as damaged, it is discarded with no notification

## Slide 46: Half-Duplex Versus Full-Duplex Communication
Half-duplex works like a two-way radio; you can talk and listen but not both at the same time
  Ethernet on hubs works only in half-duplex
Full-duplex means NIC/switch can transmit/receive simultaneously
  Like a telephone
  CSMA/CD is turned off
  Most switches operate in full-duplex
Notes: Half-Duplex Versus Full-Duplex Communication
Half-duplex works like a two-way radio; you can talk and listen but not both at the same time
  Ethernet on hubs works only in half-duplex
Full-duplex means NIC/switch can transmit/receive simultaneously
  Like a telephone
  CSMA/CD is turned off
  Most switches operate in full-duplex

## Slide 47: Ethernet Standards
Ethernet standards expressed as:
  XBaseY – 10Base2, 10BaseT, 100BaseT, 100BaseFX
  Y=2 stands for coaxil cable
  X – designates the speed of transmission
  Y – specifies the type of media (T = twisted-pair, FX = fiber optic)
10BaseT
  Uses two of the four wire pairs
  Runs over Category 3(CAT 3) or higher UTP cabling
  Highly susceptible to collisions and is obsolete
Notes: Ethernet Standards
Ethernet standards expressed as:
  XBaseY – 10Base2, 10BaseT, 100BaseT, 100BaseFX
  X – designates the speed of transmission
  Y – specifies the type of media (T = twisted-pair, FX = fiber optic)
10BaseT
  Uses two of the four wire pairs
  Runs over Category 3 or higher UTP cabling
  Highly susceptible to collisions and is obsolete

## Slide 48: Ethernet Standards
100BaseTX
  Most common Ethernet variety
  Runs over Category 5 or higher UTP
  Uses two of four wire pairs
  Two types of 100BaseTX hubs
    Class I – can have only one hub between communicating devices
    Class II – can have a maximum of two hubs between devices
  Switches can be used to interconnect multiple hubs (see slide 43)
Notes: Ethernet Standards
100BaseTX
  Most common Ethernet variety
  Runs over Category 5 or higher UTP
  Uses two of four wire pairs
  Two types of 100BaseTX hubs
    Class I – can have only one hub between communicating devices
    Class II – can have a maximum of two hubs between devices
  Switches can be used to interconnect multiple hubs

## Slide 49: Ethernet Standards
100BaseFX
  Runs over two strands of fiber optic cabling
  Typically used as backbone cabling between hubs or switches
    Also used to connect clients or servers when immunity to noise and eavesdropping is required
1000BaseT Ethernet
  Also known as “Gigabit Ethernet”
  Runs over Category 5 or higher UTP and uses all four wire pairs
Notes: Ethernet Standards
100BaseFX
  Runs over two strands of fiber optic cabling
  Typically used as backbone cabling between hubs or switches
    Also used to connect clients or servers when immunity to noise and eavesdropping is required
1000BaseT Ethernet
  Also known as “Gigabit Ethernet”
  Runs over Category 5 or higher UTP and uses all four wire pairs

## Slide 50: Ethernet Standards
10GBaseT Ethernet ( 10 gigabit )
  Runs over four pairs of Category 6A or 7 UTP
  Operates only in full-duplex mode
    No hubs, only switches support 10GBaseT
  Still considered an expensive option
  Good for network servers so they can keep up with desktop systems that commonly operate at 1 Gbps
Notes: Ethernet Standards
10GBaseT Ethernet
  Runs over four pairs of Category 6A or 7 UTP
  Operates only in full-duplex mode
    No hubs, only switches support 10GBaseT
  Still considered an expensive option
  Good for network servers so they can keep up with desktop systems that commonly operate at 1 Gbps

## Slide 51: Additional Ethernet Standards
100BaseT4
  Uses all four pairs of wires in UTP Category 3 cable
  Obsolete
1000BaseLX
  Uses fiber-optic media
  “L” stands for “long wavelength” laser
  Supports a maximum cable segment length of 5000 meters
Notes: Additional Ethernet Standards
100BaseT4
  Uses all four pairs of wires in UTP Category 3 cable
  Obsolete
1000BaseLX
  Uses fiber-optic media
  “L” stands for “long wavelength” laser
  Supports a maximum cable segment length of 5000 meters

## Slide 52: Additional Ethernet Standards
1000BaseSX
  Uses fiber-optic media
  “S” stands for “short wavelength” laser
  Can’t cover as much distance as long-wavelength lasers, but are less expensive
1000BaseCX
  Uses specially shielded, balanced, copper jumper cables
  Might also be called “twinax” or “short-haul” copper cables
Notes: Additional Ethernet Standards
1000BaseSX
  Uses fiber-optic media
  “S” stands for “short wavelength” laser
  Can’t cover as much distance as long-wavelength lasers, but are less expensive
1000BaseCX
  Uses specially shielded, balanced, copper jumper cables
  Might also be called “twinax” or “short-haul” copper cables

## Slide 53: Additional Ethernet Standards
10 Gigabit Ethernet IEEE 802.3ae
  Much like the others in frame formats and media access
  Defined to run only on fiber-optic cabling and specifies a maximum distance of 40 kilometers
  Primarily used for network backbones
  Varieties:
    10GBaseSR, 10GBaseLR, 10GBaseER, 10GBaseSW, 10GBaseLW, and 10GBaseEW
Notes: Additional Ethernet Standards
10 Gigabit Ethernet IEEE 802.3ae
  Much like the others in frame formats and media access
  Defined to run only on fiber-optic cabling and specifies a maximum distance of 40 kilometers
  Primarily used for network backbones
  Varieties:
    10GBaseSR, 10GBaseLR, 10GBaseER, 10GBaseSW, 10GBaseLW, and 10GBaseEW

## Slide 54: Additional Ethernet Standards
40 Gigabit and 100 Gigabit Ethernet
  Very high cost is still prohibitive
  Adoption has been slow
  Fiber-optic cabling is primary medium
    Although there are provisions to use special copper assemblies over short distances
Notes: Additional Ethernet Standards
40 Gigabit and 100 Gigabit Ethernet
  Very high cost is still prohibitive
  Adoption has been slow
  Fiber-optic cabling is primary medium
    Although there are provisions to use special copper assemblies over short distances

## Slide 55: Additional Ethernet Standards
Notes: Additional Ethernet Standards

## Slide 56: 802.11 Wi-Fi
The 802.11 wireless networking standard is also referred to as Wireless Fidelity (Wi-Fi)
In most towns you can usually find a public Wi-Fi network, called a hotspot
802.11 is essentially an extension to Ethernet
  Using airwaves instead of cabling as the medium
Notes: 802.11 Wi-Fi
The 802.11 wireless networking standard is also referred to as Wireless Fidelity (Wi-Fi)
In most towns you can usually find a public Wi-Fi network, called a hotspot
802.11 is essentially an extension to Ethernet
  Using airwaves instead of cabling as the medium

## Slide 57: Wi-Fi Modes of Operation
Wi-Fi can operate in one of two modes
  Infrastructure — use central access point (AP)
  Ad hoc — no central device; data travels from device to device like a bus
    Sometimes called “peer-to-peer mode”
Most of this chapter’s discussion of Wi-Fi focuses on infrastructure mode
Notes: Wi-Fi Modes of Operation
Wi-Fi can operate in one of two modes
  Infrastructure — use central access point (AP)
  Ad hoc — no central device; data travels from device to device like a bus
    Sometimes called “peer-to-peer mode”
Most of this chapter’s discussion of Wi-Fi focuses on infrastructure mode

## Slide 58
Notes: SSID = Service Set ID

## Slide 59: Wi-Fi Channels and Frequencies
Wi-Fi operate at one of two radio frequencies: 2.4GHz and 5.0 GHz
  Although this frequency is not fixed
2.4 GHz is actually 2.412 thru 2.484 divided into 14 channels spaced 5 MHz apart
  Work like a TV channel – you must tune to the correct channel to connect
  Needs 25 MHz to operate spanning 5 channels
  Choose channels five apart from other known APs
5.0 GHz is actually 4.915 thru 5.825 GHz divided into 42 channels of 10, 20, or 40 MHz each
Notes: Wi-Fi Channels and Frequencies
Wi-Fi operate at one of two radio frequencies: 2.4GHz and 5.0 GHz
  Although this frequency is not fixed
2.4 GHz is actually 2.412 thru 2.484 divided into 14 channels spaced 5 MHz apart
  Work like a TV channel – you must tune to the correct channel to connect
  Needs 25 MHz to operate spanning 5 channels
  Choose channels five apart from other known APs
5.0 GHz is actually 4.915 thru 5.825 GHz divided into 42 channels of 10, 20, or 40 MHz each

## Slide 60: Wi-Fi Channels and Frequencies
Notes: Wi-Fi Channels and Frequencies

## Slide 61: Wi-Fi Antennas
Antenna on a Wi-Fi device is both transmitter and receiver ( Full duplex )
  Characteristics and placement determine how well a device transmits or receives Wi-Fi signals
Usually categorized by their radiation pattern:
  Omnidirectional antennas – signals radiate out from the antenna with equal strength in all directions
  Unidirectional antenna – signals are focused in a single direction
    Ideal for placement at one end of long, narrow spaces
Notes: Wi-Fi Antennas
Antenna on a Wi-Fi device is both transmitter and receiver
  Characteristics and placement determine how well a device transmits or receives Wi-Fi signals
Usually categorized by their radiation pattern:
  Omnidirectional antennas – signals radiate out from the antenna with equal strength in all directions
  Unidirectional antenna – signals are focused in a single direction
    Ideal for placement at one end of long, narrow spaces

## Slide 63: Wi-Fi Access Methods and Operation
Wi-Fi Access Method
  Sending station can’t hear if another station begins transmitting so they cannot use the CSMA/CD access method that Ethernet uses
  Wi-Fi devices use carrier sense multiple access with collision avoidance (CSMA/CA)
  Uses request-to-send/clear-to-send (RTS/CTS) packets and acknowledgements
  With this extra “chatter” actual throughput is essentially cut in half
  Simulation 8 : Basic wireless LAN operation
Notes: Wi-Fi Access Methods and Operation
Wi-Fi Access Method
  Sending station can’t hear if another station begins transmitting so they cannot use the CSMA/CD access method that Ethernet uses
  Wi-Fi devices use carrier sense multiple access with collision avoidance (CSMA/CA)
  Uses request-to-send/clear-to-send (RTS/CTS) packets and acknowledgements
  With this extra “chatter” actual throughput is essentially cut in half

## Slide 64: Wi-Fi Signal Characteristics
Common types of signal interference:
  Absorption – solid objects absorb radio signals, causing them to attenuate (weaken)
  Refraction – the bending of a radio signal as it passes from a medium of one density through a medium of a different density
  Diffraction – the altering of a wave as it tries to bend around an object
  Reflection – occurs when a signal hits a dense, reflective material, resulting in signal loss
  Scattering – when a signal changes direction in unpredictable ways, causing a loss in signal strength
Notes: Wi-Fi Signal Characteristics
Common types of signal interference:
  Absorption – solid objects absorb radio signals, causing them to attenuate (weaken)
  Refraction – the bending of a radio signal as it passes from a medium of one density through a medium of a different density
  Diffraction – the altering of a wave as it tries to bend around an object
  Reflection – occurs when a signal hits a dense, reflective material, resulting in signal loss
  Scattering – when a signal changes direction in unpredictable ways, causing a loss in signal strength

## Slide 65: Wi-Fi Signal Characteristics
Signal-to-noise ratio(SNR,S/N) – the amount of noise compared with the signal strength
  Noise can come from equipment, other wireless devices, and other wireless networks
Throughput – the actual amount of data transferred
  Not counting errors and acknowledgements
Goodput – actual application-to-application data transfer speed
Overhead – packet frame headers, acknowledgements, and retransmissions
Notes: Wi-Fi Signal Characteristics
Signal-to-noise ratio – the amount of noise compared with the signal strength
  Noise can come from equipment, other wireless devices, and other wireless networks
Throughput – the actual amount of data transferred
  Not counting errors and acknowledgements
Goodput – actual application-to-application data transfer speed
Overhead – packet frame headers, acknowledgements, and retransmissions

## Slide 66: Wi-Fi Standards
Notes: Wi-Fi Standards

## Slide 67: What is non-overlapping channel?
For example 802.11b and g has 14 channels
1, 6, 11 are non-overlapping
2, 7, 12 are non-overlapping
4, 8, 13 are non-overlapping etc.

## Slide 68: Wi-Fi Security
Signals from a Wi-Fi network can travel several hundred feet – Wi-Fi devices outside your home or business can detect your signals
Wi-Fi network should be protected by an encryption protocol that makes data difficult to interpret
Encryption protocols
  Wired equivalent privacy (WEP), Wi-Fi Protected Access (WPA), and WPA2,
  Not all devices support all three protocols
    Older devices might only support WEP and/or WPA
Notes: Wi-Fi Security
Signals from a Wi-Fi network can travel several hundred feet – Wi-Fi devices outside your home or business can detect your signals
Wi-Fi network should be protected by an encryption protocol that makes data difficult to interpret
Encryption protocols
  Wired equivalent privacy (WEP), Wi-Fi Protected Access (WPA), and WPA2,
  Not all devices support all three protocols
    Older devices might only support WEP and/or WPA

## Slide 69: Token Ring Networks
Based on the IEEE 802.5 standard
Star physical topology, ring logical topology
A token is passed along the network
  Only the station with the token can transmit
  Frames are acknowledged and token is released
  No collisions
Originally operated at 4Mbps and then increased to 16 Mbps and later 100 Mbps
Uses cat 4 and higher UTP
Obsolete
Notes: Token Ring Networks
Based on the IEEE 802.5 standard
Star physical topology, ring logical topology
A token is passed along the network
  Only the station with the token can transmit
  Frames are acknowledged and token is released
  No collisions
Originally operated at 4Mbps and then increased to 16 Mbps and later 100 Mbps
Uses cat 4 and higher UTP
Obsolete

## Slide 70: Fiber Distributed Data Interface Technology
Physical and logical ring topology
Uses a token-passing access method and dual rings for redundancy
Transmits at 100 Mbps and can include up to 500 nodes over a distance of 60 miles
Uses fiber-optic cable only
Obsolete on new networks
Notes: Fiber Distributed Data Interface Technology

## Slide 71: Summary
Networks can be described by a physical and logical topology
The primary physical topologies are the bus, star, ring, meshed and point-to-point
The primary logical topologies are bus, ring, and switched
A network technology defines the structure of the frames and how a network interface access the medium to send data frames
Notes: Summary
Networks can be described by a physical and logical topology
The primary physical topologies are the bus, star, ring, and point-to-point
The primary logical topologies are bus, ring, and switched
A network technology defines the structure of the frames and how a network interface access the medium to send data frames

## Slide 72: Summary
The most common network technology for LANs is Ethernet
Wi-Fi is a wireless technology based on Ethernet but uses the CSMA/CA media access method
The antenna on a Wi-Fi device is both the transmitter and receiver
Wi-Fi signal interference can severely affect a WLAN’s performance and reliability
Token Ring and FDDI are both obsolete technologies that used a token passing access method
Notes: Summary
The most common network technology for LANs is Ethernet
Wi-Fi is a wireless technology based on Ethernet but uses the CSMA/CA media access method
The antenna on a Wi-Fi device is both the transmitter and receiver
Wi-Fi signal interference can severely affect a WLAN’s performance and reliability
Token Ring and FDDI are both obsolete technologies that used a token passing access method