## Slide 1: Topic 1b : Network Protocols
Remote Desktop
Address Resolution Protocol (ARP)
Domain Name System (DNS)
Simple Network Management Protocol (SNMP)
Basic Ping sweeps and Port scans
Banner grabbing

## Slide 2: Remote Desktops
Allows a computer’s desktop environment to be viewed or controlled remotely
Used by IT support to troubleshoot computer problems
Can also be used by hackers impersonating IT support staff and getting users to allow remote desktop access
Remote Access Trojan (RAT) : malware that allows a hacker to control a computer remotely

## Slide 3: Remote Desktop Software
Remote Desktop Services (Microsoft)
TeamViewer
TightVNC (based on Virtual Network Computing)
And more

## Slide 4: Remote Desktop Services
Microsoft’s Remote Desktop Connection
Allows users to connect remotely to Windows system
Runs on TCP Port 3389
If Remote Desktop Connection is needed, use Network Level Authentication for more security

## Slide 5: Address Resolution Protocol (ARP)
For a device to send a packet to another device on the same local network, it needs the MAC address of the destination
ARP is the protocol used to find the MAC address

## Slide 6: Address Resolution Protocol (ARP)
To find the MAC address of an IP address
  The sender will look at its ARP table
  If the IP address is not listed in the ARP table, the sender will send an ARP broadcast to all devices in the local network to ask who has that IP address
  The device with the IP address will send an ARP reply to the sender with its MAC address
  The sender will send the packet to this MAC address
  The sender will update its ARP table with this MAC address in case it needs to send more packets to it again

## Slide 7: Address Resolution Protocol (ARP)
In this example, the sender (192.168.10.88) wants to send a packet to 192.168.6.53
In the first packet, the sender sends an ARP broadcast to all devices in the same local network to ask who has the IP 192.168.6.53
In the second packet, the device with IP 192.168.6.53 sends an ARP reply with its MAC address 00:0C:29:19:0C:CA

## Slide 8: ARP poisoning / spoofing
If the attacker can “poison” the ARP table, he can cause devices to send packets to him instead
Normal Scenario :
  Computer A will record in its ARP table
  IP MAC
  192.168.1.30 11-22-11-22-11-22
  Packets addressed to IP 192.168.1.30 will be sent to MAC address11-22-11-22-11-22
Computer A
Computer B
IP : 192.168.1.30
MAC : 11-22-11-22-11-22
ARP broadcast : Who has IP 192.168.1.30?
ARP reply: IP 192.168.1.30 is at MAC 11-22-11-22-11-22

## Slide 9: ARP poisoning / spoofing
Attack Scenario :
The attacker quickly replies to Computer A with his MAC address before Computer B can reply
  Computer A will record the wrong MAC address in its ARP table
  IP MAC
  192.168.1.30 66-77-66-77-66-77
  Packets addressed to IP 192.168.1.30 will be sent to the attacker instead
Computer A
Attacker
MAC : 66-77-66-77-66-77
ARP broadcast : Who has IP 192.168.1.30?
ARP reply: IP 192.168.1.30 is at MAC 66-77-66-77-66-77

## Slide 10: Domain Name System (DNS)
When browsing the Internet, users enter domain names like www.google.com or www.sp.edu.sg
DNS will resolve these domain names to their IP addresses

## Slide 11: Domain Name System (DNS)
The DNS Server (or nameserver) contains a database that holds a section of domain names mapped to IP addresses.
  Eg. A DNS Server can be responsible for the domain names under abc.com
  The DNS server may have the following records.
  station1.abc.com 192.168.0.1
  station2.abc.com 192.168.0.2
  station3.abc.com 192.168.0.3

## Slide 12: DNS poisoning / spoofing
If the attacker can edit the DNS database or DNS cache, he can direct users to his own website instead
Example :
  Users who try to browse to www.yahoo.com will go to the website at 192.168.0.13 instead
Proper configuration of the DNS can reduce risks of such attacks
“Poisoned” DNS Server
DNS cache maps www.yahoo.com to the attacker’s IP (192.168.0.13) instead :
Domain IP
www.yahoo.com 192.168.0.13

## Slide 13: Simple Network Management Protocol (SNMP)
For remote monitoring and management of network nodes
SNMP manager monitors a set of SNMP agents installed on network nodes
  Checks performance of monitored nodes
  Makes changes in configuration of monitored nodes
SNMP agent can send warning to SNMP manager of unusual situations
Do the SNMP Quiz in BlackBoard

## Slide 14: Ping sweeps
A ping sweep sends ping packets to a range of IP addresses to see which system will reply
  ping 192.168.1.1
  ping 192.168.1.2
  ping 192.168.1.3
Can be used to see which system is alive
Also known as ICMP sweep

## Slide 15: Basic port scan with Nmap
To test if a port is opened, a SYN packet can be sent to the port
If a SYN/ACK packet is returned, the port is opened
Nmap is a popular tool to scan for opened ports
Scanner
Web Server running on Port 80
SYN packet sent to Port 80
SYN/ACK packet returned

## Slide 16: Banner Grabbing
Many services return information like version number when a client connects to it (a “banner”)
Banner grabbing is a method hackers can use to find more information about a running service
Usually telnet or netcat (nc) is used to do banner grabbing
From this banner returned by an Apache Web Server, we know it is version 2.2.15 and running on Red Hat Linux

## Slide 17: Topic 1b Network Protocols Summary
Remote Desktop for remote logins
ARP
  ARP Spoofing and SSL Strip (practical)
DNS
  DNS Chef to redirect users to wrong websites (practical)
SNMP (online quiz)
Ping sweeps
Basic port scans
Banner Grabbing