## Slide 1: Topic 5 Firewalls
ST251Y Ethical Hacking and Defences

## Slide 2: Topic 5 : Firewalls
Understand Network Address Translation (NAT)
Understand the use of Proxy Servers
The Demilitarized Zone (DMZ), Bastion Hosts and Honeypots
Explain what firewalls can and cannot do
Describe common approaches to packet filtering
Establish a set of rules and restrictions for a firewall
Explore common firewall configurations
Compare hardware and software firewalls

## Slide 3: Network Address Translation (NAT)
A network device (usually a firewall or proxy server) hides internal IP addresses from the outside world
A public IP address is presented to the outside world
Internal PC 192.168.2.4
Internal PC 192.168.2.5
Internal PC 192.168.2.6
Firewall with NAT
Internal IP : 192.168.2.100
External IP : 164.78.5.69
The internal IPs 192.168.2.n are hidden from the outside world
Only the public IP 164.78.5.69 is seen by outside networks

## Slide 4: Why NAT?
Reduces the number of public IP addresses required by an organisation
  Hundreds or even thousands of internal computers can be behind a single public IP address
Internal IP addresses are hidden from outside attackers

## Slide 5: How does NAT work?
When an internal computer wants to request a web page from a web server on the Internet, its packets goes to the NAT device first
Internal IP 10.0.20.11
External IP 211.24.120.5
Web Server 68.29.12.56
NAT device
Computer A sends a packet
Source IP : 10.0.20.28
Dest IP : 68.29.12.56
Computer A
10.0.20.28

## Slide 6: How does NAT work?
The NAT device will replace the source IP with its public IP address and sends the packet to the web server on the Internet
Internal IP 10.0.20.11
External IP 211.24.120.5
Web Server 68.29.12.56
NAT device
Computer A
10.0.20.28
NAT Device sends the packet to Web Server
Source IP : 211.24.120.5
Dest IP : 68.29.12.56

## Slide 7: How does NAT work?
The web server only sees the public IP address. It will send its packets to the NAT device
Internal IP 10.0.20.11
External IP 211.24.120.5
Web Server 68.29.12.56
NAT device
Computer A
10.0.20.28
Web Server responds with a packet for NAT device
Source IP : 68.29.12.56
Dest IP : 211.24.120.5

## Slide 8: How does NAT work?
The NAT device will remember which internal computer requested for the web page and sends the packet accordingly
Internal IP 10.0.20.11
External IP 211.24.120.5
Web Server 68.29.12.56
NAT device
Computer A
10.0.20.28
NAT Device forwards packet to Computer A
Source IP : 68.29.12.56
Dest IP : 10.0.20.28

## Slide 9: Proxy Server
A proxy server intercepts internal user requests and processes that request on behalf of the user
Web Server
Proxy Server
1. User requests for web page
2. Proxy Server connects to Web Server to request for web page
3. Web Server returns web page to Proxy Server
4. Proxy Server forwards web page to user

## Slide 10: Proxy Server
The Proxy Server keeps a cache of the retrieved web pages
  Other users requesting for the same pages can retrieve them from the Proxy Server cache
  Faster retrieval time
Proxy Servers can filter web content
  Block access to undesirable websites
  Keeps log of websites accessed by users

## Slide 11: Proxy Server
Proxy servers can also be used to hide IP addresses

## Slide 12: How Proxy Servers work
Proxy servers prevent direct connections between external computers and internal computers
Proxy servers work at the application layer
  Examines the data in the packet
  Decides to which application or system to forward the packet to
  Reconstructs the packet and forwards it
    Replace the original header with a new header containing proxy’s own IP address

## Slide 13
Web Server
IP : 89.19.30.6
Proxy Server
1. User requests for web page
2. Proxy Server connects to Web Server to request for web page on behalf of the user
Internal IP : 192.168.7.1
External IP : 209.18.7.48
User sends packet requesting for web page
Src IP : 192.168.7.14
Dest IP : 89.19.30.6
User
IP : 192.168.7.14
Proxy Server sends packet requesting for web page
Src IP : 209.18.7.48
Dest IP : 89.19.30.6

## Slide 14
Web Server
IP : 89.19.30.6
Proxy Server
3. Web Server returns web page to Proxy Server
4. Proxy Server forwards web page to user
Internal IP : 192.168.7.1
External IP : 209.18.7.48
Proxy Server forwards packet containing web page to User
Src IP : 89.19.30.6
Dest IP : 192.168.7.14
User
IP : 192.168.7.14
Wed Server returns packet containing web page
Src IP : 89.19.30.6
Dest IP : 209.18.7.48

## Slide 15: Connecting to Proxy Servers
Client programs (eg web browsers) can be configured to connect to the proxy server instead of the Internet
Transparent proxy servers (or intercepting proxies) do not require the client to be specially configured

## Slide 17: Choosing a Proxy Server
Freeware proxy servers
  Often described as content filters
  May not have advanced features
  Example: Squid
Commercial proxy servers
  Offer Web page caching, source and destination IP addresses translation, content filtering, and NAT
  Example: Many hardware firewalls come with proxy server functionality

## Slide 18: Reverse Proxy
A reverse proxy is used to help the web server
  Can offload some of the load on the web server by caching static web content
  Can perform load balancing among multiple web servers
  Can handle the SSL encryption, freeing the web servers from doing the encryption/decryption of data
Web Server 1
Reverse Proxy
Web Server 2
Clients

## Slide 20: DMZ
Normally all internal computers are kept inaccessible from the Internet
But public users will need to access some resources like Web Servers
The DMZ (Demilitarized zone) is a section of the network that is visible to the outside world
Public users can access the DMZ but cannot enter the internal secured network
May also be called service network or perimeter network

## Slide 22: Bastion Host
Normally refers to a computer that has been specially protected through OS patches, authentication, encryption, etc
Such specially secured computers are normally those at the network perimeter (may be in the DMZ)
Usually provides Web, FTP, e-mail, or other services running on a specially secured server

## Slide 24: Honeypot
Computer placed on the network perimeter
Attracts attackers away from real and critical servers
Another goal of a honeypot is logging
  Logs are used to learn about attackers’ techniques
Legal issues
  Example : what if the attacker uses your purposely unsecured honeypot to harm other networks?

## Slide 26: Overview of firewalls
Firewall
  Hardware or software
  To block unauthorized network access
Earliest firewalls were packet filters
Firewall
Packet
Packet accepted
Packet blocked

## Slide 27: Firewall rules
Firewalls can be configured by setting rules
Rules for blocking traffic may be done case-by-case
  Actions include:
    Allow the traffic
    Block the traffic
    Customize access (eg forward packet to another set of rules for further processing)

## Slide 29: What firewalls can’t do
Firewalls cannot protect connections that do not go through it
Firewall
Employee sets up illegal access point that is not secured
Hacker accesses network through illegal access point, bypassing firewall

## Slide 30: Personal Firewalls
Some firewalls are designed for personal use
  Norton Internet Security
  ZoneAlarm

## Slide 31: Enterprise Firewalls
Some firewalls are designed for company/enterprise use
For monitoring and protecting large-scale networks
Manage security policies throughout the organisation

## Slide 32: Firewalls only a part of security solution
Firewalls are not a standalone solution
  Cannot protect from internal threats
  Need strong security policy and employee education
Firewalls must be combined with other security solutions
  Antivirus software
  Intrusion Detection Systems

## Slide 33: Packet Filtering
Only info in packet headers are checked
Data in packets not checked
Stateless packet filtering
Stateful packet filtering

## Slide 34: Stateless Packet Filtering
Decides whether to allow or block packets based only on information in the protocol headers
Filtering based on common IP header features
  IP address and Ports
  Protocols
  Flags and options
Advantage: Inexpensive and fast
Disadvantage: Attacks nowadays are more complicated

## Slide 36: Stateful Packet Filtering
Besides looking at information in the protocol headers, keeps a record of connections the host computer has made with other computers
  Maintain a file called a state table containing a record of all current connections
  Allows incoming packets to pass through only from external hosts already connected

## Slide 38: Typical locations of Packet Filters
Packet filter placement
  Between the Internet and a host/network
  Between a proxy server and the Internet
  At either end of a DMZ

## Slide 41: Application Layer Firewall
Inspects both header and data portions of packets
Also known as content filtering
Application Layer Firewalls can check for malicious code contains in the packet data
Combination of packet filters and application layer firewalls can be used in a network

## Slide 42: Configuring Firewall rules
Rule base
  Tells firewalls what to do when a certain kind of traffic attempts to pass
Points to consider
  Based on organization’s security policy
  Determine what can be accessed from external network
  Logging and auditing requirements
  Network Address Translation (NAT), if used
  Simple and short as possible – firewall should not cause too much delay in network speed, and should be easy to maintain

## Slide 43: Base Firewall Rules on Security Policy
Examples of common security policies to be reflected in the firewall rules (different companies will have different security policies)
  Employees have access to Internet with restrictions
  Public can access company’s Web and e-mail server
  Only authenticated traffic can access the internal LAN
  Employees are not allowed to use instant-messaging
  Traffic from the company’s ISP should be allowed
  Block external traffic by instant-messaging software
  Only network administrator should be able to access internal network directly from the Internet

## Slide 44: Keep the rule base simple
Keep list of rules as short as possible
  So firewall will perform faster
Firewalls process rules in a particular order
  If the rules are numbered, the firewall will match packets with the first rule, then the second rule, and so on
  Most important and frequently-accessed rules should be at the top of the list
  Make the last rule a cleanup rule
    A catch-all type of rule

## Slide 45: Firewall Rules
 | Source IP | Source Port | Dest IP | Dest Port | Action
1 | Any | Any | 192.168.1.10 | 80 | Allow
2 | 192.168.3.0/24 | Any | 192.168.1.24 | 22 | Allow
3 | 192.168.3.10 | Any | 192.168.1.24 | 22 | Deny
4 | Any | Any | Any | Any | Deny
Incoming
Rule 3 will never be activated, because Rule 2, which is processed first, will allow the packets
Rule 3 should be placed before Rule 2
Rule 4 is the cleanup rule – deny all other traffic

## Slide 47: Restrict Subnets, Ports, and Protocols
You can filter by
  IP addresses
  Ports
Some firewalls can filter by the name of a service (no need to remember port number)
Some firewalls can also filter by the six TCP control flags or by IP options

## Slide 48: General Practices
Rules should follow a few general practices
  Most frequently matched rules should be near the top of the rule base for faster processing
  Nobody can connect to the firewall except the administrator
  Block direct access from the Internet to any computer behind the firewall
  Permit access to public services in the DMZ

## Slide 49
Subnet of Company
Firewall IP : 192.168.120.1

## Slide 50
Mail Server IP : 192.168.120.2
Web Server IP : 192.168.120.3
With Rule 3, do we need Rules 4 and 6?

## Slide 51: Anti-Spoofing Rule
In many firewall configurations, the first rule is the Anti-Spoofing rule.
The anti-spoofing rule blocks packets coming from outside network pretending to be an internal system
Computer 1
192.168.1.10
Computer 2
192.168.1.20
Hacker pretending
to be Computer 1
Packet
Source : 192.168.1.10
Destination : 192.168.1.20
Firewall drops packet because packets from Computer 1 should not be coming in from outside

## Slide 52: Firewall Rule Matching
Firewalls match packets to rules in a particular order
  Once a rule is matched, the packet is processed according to the action specified in the rule (usually to allow or block the packet)
For firewalls with numbered rules, the packets are matched to rules according to the Rule Numbers.
Rule Numbers

## Slide 53: Firewall Rule Matching
Other firewalls will match the Deny rules first, then match the Allow rules
Packets that do not match any rules will follow the firewall’s default policy action (normally set to Deny any packet that is not explicitly allowed)
The Block rule will take precedence and be matched to ICMP packets first.

## Slide 54: Firewall Logs
Decide what to log
  Some firewalls log only packets associated with a Deny rule (eg blocked IP addresses)
Configuring the log file format
  Many firewalls generate log files in plain text
  Sophisticated firewalls save log files in other formats
Review log files regularly
Log files can indicate signatures of attack attempts

## Slide 55: Firewall Logs
Preparing log file summaries and generating reports
  Log summary
    Shows major events over a period of time
    Contain raw data that can be used to create reports
  Some firewalls contain log file analysis tools
    Viewing raw data can be tedious and prone to errors
  Reports
    Display data in an easy-to-read format

## Slide 56: Designing Firewall Configurations
Firewalls can be deployed in several ways
  As part of a screening router
  Dual-homed host
  Screen host
  Screened subnet DMZ
  Multiple DMZs
  Multiple firewalls
  Reverse firewall
There can be other methods of deploying firewalls
  Depends on the company’s network and needs

## Slide 57: Screening Router
Screening router
  Determines whether to allow or deny packets based on their source and destination IP addresses
    Or other information in their headers
  Does not stop many attacks
    Especially those that use spoofed or manipulated IP address information
  Should be combined with a firewall or proxy server
    For additional protection

## Slide 59: Dual-Homed Host
Dual-homed host
  Computer that has been configured with more than one network interface
  Firewall software forwards packets from one network interface to another
  Provides limited security
  Host serves as a single point of entry to the organization

## Slide 61: Screened Host
Screened host
  Similar to a dual-homed host
  Can add router between the host and the Internet
    To carry out IP packet filtering
  Combines a dual-homed host and a screening router
  Can function as a gateway or proxy server

## Slide 63: Screened Subnet DMZ
DMZ
  Subnet of publicly accessible servers placed outside the internal LAN
  Called a “service network” or “perimeter network”
Firewall that protects the DMZ is connected to the Internet and the LAN
  Called a three-pronged firewall

## Slide 65: Multiple DMZ/Firewall Configurations
Server farm
  Group of servers connected in their own subnet
  Work together to receive requests with the help of load-balancing software
Load-balancing software
  Prioritizes and schedules requests and distributes them to servers
Clusters of servers in DMZs help protecting the network from becoming overloaded
Each server farm/DMZ can be protected with its own firewall or packet filter

## Slide 67: Multiple Firewall Configurations
Protecting a DMZ with two or more firewalls
  One firewall controls traffic between DMZ and Internet
  Second firewall controls traffic between protected LAN and DMZ
    Can also serve as a failover firewall
  Advantage
    Can control where traffic goes in the three networks you are dealing with

## Slide 68: Multiple Firewall Configurations (continued)
Additional firewall placed inside internal network to protect network management systems
  Extra level of protection for network management systems
  Intruders that gain control of network management system can potentially gain access to all network

## Slide 70: Multiple Firewall Configurations (continued)
Protecting branch offices with multiple firewalls
  Multiple firewalls can implement a single security policy
  Central office has a centralized firewall
    Directs traffic for branch offices and their firewalls
    Deploys security policy through this firewall using a security workstation

## Slide 73: Comparing Software and Hardware Firewalls
Software-based firewalls
Hardware-based firewalls
Hybrid firewalls

## Slide 74: Software-Based Firewalls
Free firewall programs
Commercial firewall programs for personal use
Commercial firewall programs for enterprise use
  Capable of managing multiple instances from a centralized location

## Slide 75: Hardware Firewalls
Also called firewall appliances
Advantages
  Do not depend on conventional OSs
  Generally more scalable than software firewalls
Disadvantages
  They do depend on nonconventional OSs
  Tend to be more expensive than software products

## Slide 76: Hybrid Firewalls
Hybrid firewall
  Combines aspects of hardware and software firewalls
  Benefits from the strengths of both solutions

## Slide 78: Summary
Understand Network Address Translation (NAT)
Understand the use of Proxy Servers
The Demilitarized Zone (DMZ), Bastion Hosts and Honeypots
Explain what firewalls can and cannot do
Describe common approaches to packet filtering
Establish a set of rules and restrictions for a firewall
Explore common firewall configurations
Compare hardware and software firewalls