## Slide 1: Guide to Networking Essentials 7th Edition
Topic 02
Network Media
Notes: Network+ Guide to Networks 7th Edition
Chapter 4
Network Media

## Slide 2: Objectives
Define the primary cables used in wired networking
Describe the characteristics of the major types of fiber-optic media
Explain the technologies used for wireless networking
Notes: Objectives
Define the primary cables used in wired networking
Describe the characteristics of the major types of fiber-optic media
Explain the technologies used for wireless networking

## Slide 3: Wired Networking
Wired networking uses tangible physical media called cables
Two broad categories of cables: copper wire and fiber optic
The main differences between the two types:
  Composition of signals (electricity or light)
  Speed at which signals can be sent
  Distance the signals can effectively travel
Notes: Wired Networking
Wired networking uses tangible physical media called cables
Two broad categories of cables: copper wire and fiber optic
The main differences between the two types:
  Composition of signals (electricity or light)
  Speed at which signals can be sent
  Distance the signals can effectively travel

## Slide 4: Criteria for Choosing Network Media
Bandwidth Rating – number of bits per second that can be transmitted across a medium
  A factor determining bandwidth is how bit signals are represented on the medium (called encoding – next slide)
  When possible, choose a cabling category that’s compatible with the standard you want to implement now but will support growth and faster speeds
Maximum Segment Length – maximum length of cable between two network devices
  Each cable type can transport data only so far before its signals begin to weaken beyond what can be read by a receiving device (called attenuation)
Notes: Criteria for Choosing Network Media
Bandwidth Rating – number of bits per second that can be transmitted across a medium
  A factor determining bandwidth is how bit signals are represented on the medium (called encoding)
  When possible, choose a cabling category that’s compatible with the standard you want to implement now but will support growth and faster speeds
Maximum Segment Length – maximum length of cable between two network devices
  Each cable type can transport data only so far before its signals begin to weaken beyond what can be read by a receiving device (called attenuation)

## Slide 5: Digital Signal Encoding
Notes: Not tested – for general knowledge
NRZ-L: low voltage = 1, high voltage = 0
NRZ-I: transition = 1, no transition = 0
Manchester: transition at mid bit second from low to high = 1, transition at mid bit second from high to low = 0
For NRZ-L and NRZ-I, transmitting continuously “0s” or “1s” may cause sender and receiver to loose synchronisation. Must pause in between to allow sender and receiver to resynchronise.
Whereas for Manchester encoding sender and receiver are always synchronise because there is always a transition at the mid bit second for every single bit.

## Slide 6: Criteria for Choosing Network Media
Maximum Segment Length – maximum length of cable between two network devices (called cable segment)
  Any intermediate passive devices, such as wall jacks, are part of the total segment length (see slide 25)
  Each cable type can transport data only so far before its signals begin to weaken beyond what can be read by a receiving device (called attenuation)
Notes: Criteria for Choosing Network Media
Maximum Segment Length – maximum length of cable between two network devices (called cable segment)
  Any intermediate passive devices, such as wall jacks, are part of the total segment length
  Each cable type can transport data only so far before its signals begin to weaken beyond what can be read by a receiving device (called attenuation)

## Slide 7: Criteria for Choosing Network Media
Interference and Eavesdropping Susceptibility
  Interference to electrical signals on copper media comes in the form of electromagnetic interference (EMI) and radio frequency interference (RFI)
    Motors, transformers, fluorescent lights and other sources of intense electrical activity can emit both EMI and RFI.
    RFI can also affect wireless networks if the frequencies are in the same range
  Crosstalk - interference one wire generates on another wire when both wires are in a bundle
  Copper wire is susceptible to electronic eavesdropping
  Fiber-optic media carries light signals and is not susceptible to interference or eavesdropping
Notes: Criteria for Choosing Network Media
Interference and Eavesdropping Susceptibility
  Interference to electrical signals on copper media comes in the form of electromagnetic interference (EMI) and radio frequency interference (RFI)
    Motors, transformers, fluorescent lights and other sources of intense electrical activity can emit both EMI and RFI.
    RFI can also affect wireless networks if the frequencies are in the same range
  Crosstalk - interference one wire generates on another wire when both wires are in a bundle
  Copper wire is susceptible to electronic eavesdropping
  Fiber-optic media carries light signals and is not susceptible to interference or eavesdropping

## Slide 8: Criteria for Choosing Network Media
Cable Grade
  Building and fire codes include specific cabling requirements
  Cables ran between a false ceiling and the true ceiling (plenum) must be plenum-rated
  UTP Cabling is marked as communication cable riser (CMR) or communication cable plenum (CMP)
  CMR can only be used for building risers or in cable trays
  CMP is suitable for use in plenum spaces
Notes: Criteria for Choosing Network Media
Cable Grade
  Building and fire codes include specific cabling requirements
  Cables ran between a false ceiling and the true ceiling (plenum) must be plenum-rated
  UTP Cabling is marked as communication cable riser (CMR) or communication cable plenum (CMP)
  CMR can only be used for building risers or in cable trays
  CMP is suitable for use in plenum spaces
  A space lying above the ceiling in a building but below the next floor, especially oneallowing movement of air between parts of the building.

## Slide 9: Criteria for Choosing Network Media
Connection Hardware
  Every type of cable has connectors that influence the kinds of hardware the cable can connect to
  You must make sure the media you select can be supported by the network device
Notes: Criteria for Choosing Network Media
Connection Hardware
  Every type of cable has connectors that influence the kinds of hardware the cable can connect to
  You must make sure the media you select can be supported by the network device

## Slide 10: Other Media Considerations
Ease of installation – factors to consider:
  Media’s minimum bend radius, which limits the angle at which a cable can be bent to run around corners
  Cost and time needed to terminate the medium
  Physical environment – types of walls and ceilings, EMI or RFI
Testability – A network that “works” might be crippled by excessive errors
  It is important to certify whether the cable meets requirements for its category
Total cost – includes cabling, connectors, termination panels, wall jacks, termination tools, testing equipment and time
Notes: Other Media Considerations
Ease of installation – factors to consider:
  Media’s minimum bend radius, which limits the angle at which a cable can be bent to run around corners
  Cost and time needed to terminate the medium
  Physical environment – types of walls and ceilings, EMI or RFI
Testability – A network that “works” might be crippled by excessive errors
  It is important to certify whether the cable meets requirements for its category
Total cost – includes cabling, connectors, termination panels, wall jacks, termination tools, testing equipment and time

## Slide 11: Coaxial Cable
Often called “coax” for short
Once was the predominant form of network cabling
Inexpensive and easy to install
Started to phase out in the early 1990’s
Still used primarily in connecting a cable modem to the wall outlet your cable TV/Internet provider installs
Notes: Coaxial Cable
Often called “coax” for short
Once was the predominant form of network cabling
Inexpensive and easy to install
Started to phase out in the early 1990’s
Still used primarily in connecting a cable modem to the wall outlet your cable TV/Internet provider installs

## Slide 12: Twisted-Pair Cable
Comes in two types: unshielded and shielded
Consists of one or more pairs of insulated strands of copper wires twisted around one another and housed in an outer jacket
Twists are necessary to improve resistance to crosstalk from wires and EMI from outside sources
  The more twists per unit length, the better resistance to EMI and crosstalk
  More expensive TP is twisted more than less expensive and provides a better pathway for higher bandwidth networks
Notes: Twisted-Pair Cable
Comes in two types: unshielded and shielded
Consists of one or more pairs of insulated strands of copper wires twisted around one another and housed in an outer jacket
Twists are necessary to improve resistance to crosstalk from wires and EMI from outside sources
  The more twists per unit length, the better resistance to EMI and crosstalk
  More expensive TP is twisted more than less expensive and provides a better pathway for higher bandwidth networks

## Slide 13: Twisted-Pair Cable
Notes: Twisted-Pair Cable

## Slide 14: Unshielded Twisted-Pair Cable
Most networks use Unshielded Twisted-Pair (UTP)
Consists of four pairs of insulated wires
Rated according to categories devised by the Telecommunications Industry Association (TIA) and Electronic Industries Alliance (EIA) and American National Standards Institutes (ANSI)
Categories 1 – 6a are accepted in US
Two additional categories aren’t yet TIA/EIA standards and might never be in US
  Europe has accepted Category 7 and 7a, which specify that each wire pair is shielded
Notes: Unshielded Twisted-Pair Cable
Most networks use Unshielded Twisted-Pair (UTP)
Consists of four pairs of insulated wires
Rated according to categories devised by the Telecommunications Industry Association (TIA) and Electronic Industries Alliance (EIA) and American National Standards Institutes (ANSI)
Categories 1 – 6a are accepted in US
Two additional categories aren’t yet TIA/EIA standards and might never be in US
  Europe has accepted Category 7 and 7a, which specify that each wire pair is shielded

## Slide 15: Categories of UTP Cables

## Slide 16: Unshielded Twisted-Pair Cable
Categories 5e and 6 UTP Cabling Characteristics
  These categories are the most popular types of UTP cabling in today’s networks
Notes: Unshielded Twisted-Pair Cable
Categories 5e and 6 UTP Cabling Characteristics
  These categories are the most popular types of UTP cabling in today’s networks

## Slide 17: Shielded Twisted-Pair Cable
Includes shielding to reduce crosstalk and interference
  Has a wire braid inside the sheath material or a foil wrap
  Best to use in electrically noisy environments or very high-bandwidth applications
Notes: Shielded Twisted-Pair Cable
Includes shielding to reduce crosstalk and interference
  Has a wire braid inside the sheath material or a foil wrap
  Best to use in electrically noisy environments or very high-bandwidth applications

## Slide 18: Twisted-Pair Cable Plant Components
RJ-45 Connectors – STP and UTP uses registered jack 45 (RJ-45)
  Most commonly used in patch cables, which are used to connect computers to hubs, switches, and RJ-45 wall jacks
RJ-45 jacks – what you plug an RJ-45 connector into when the computer is not near a switch or hub
  Usually placed behind wall plates when cables are run inside walls
Notes: Twisted-Pair Cable Plant Components
RJ-45 Connectors – STP and UTP uses registered jack 45 (RJ-45)
  Most commonly used in patch cables, which are used to connect computers to hubs, switches, and RJ-45 wall jacks

## Slide 19: Twisted-Pair Cable Plant Components
Patch cable – short cable for connecting a computer to an RJ-45 wall jack or connecting a patch-panel port to a switch or hub
  Can be made with inexpensive tools, two RJ-45 plugs and a length of TP cable
Notes: Twisted-Pair Cable Plant Components
Patch cable – short cable for connecting a computer to an RJ-45 wall jack or connecting a patch-panel port to a switch or hub
  Can be made with inexpensive tools, two RJ-45 plugs and a length of TP cable

## Slide 20: Twisted-Pair Cable Plant Components
Patch Panels – used to terminate long runs of cable from where the computers are to the wiring closet (where the switches and hubs are)
Notes: Twisted-Pair Cable Plant Components
Patch Panels – used to terminate long runs of cable from where the computers are to the wiring closet (where the switches and hubs are)
Distribution racks – hold network equipment such as routers and switches, plus patch panels and rack-mounted servers
  Also called 19” racks because the upright rails are 19” apart

## Slide 21: Twisted-Pair Cable Plant Components
Distribution racks – hold network equipment such as routers and switches, plus patch panels and rack-mounted servers
  Also called 19” racks because the upright rails are 19” apart
Notes: Twisted-Pair Cable Plant Components
Patch Panels – used to terminate long runs of cable from where the computers are to the wiring closet (where the switches and hubs are)
Distribution racks – hold network equipment such as routers and switches, plus patch panels and rack-mounted servers
  Also called 19” racks because the upright rails are 19” apart

## Slide 22: Structured Cabling: Managing and Installing a UTP Cable Plant
Structured cabling specifies how cabling should be organized, regardless of the media type or network architecture
Large networks typically use most or all of these:
  Work area
  Horizontal wiring
  Telecommunication closets
  Equipment rooms
  Backbone or vertical wiring
  Entrance facilities
Notes: Structured Cabling: Managing and Installing a UTP Cable Plant
Structured cabling specifies how cabling should be organized, regardless of the media type or network architecture
Large networks typically use most or all of these:
  Work area
  Horizontal wiring
  Telecommunication closets
  Equipment rooms
  Backbone or vertical wiring
  Entrance facilities

## Slide 23: Structured Cabling: Managing and Installing a UTP Cable Plant
Work Area – where workstations and other user devices are located
  Faceplates and wall jacks are installed in the work area
  Patch cable connect computers and printers to wall jacks
Notes: Structured Cabling: Managing and Installing a UTP Cable Plant
Work Area – where workstations and other user devices are located
  Faceplates and wall jacks are installed in the work area
  Patch cable connect computers and printers to wall jacks

## Slide 24: Structured Cabling: Managing and Installing a UTP Cable Plant
Horizontal wiring – runs from the work area’s wall jack to the telecommunication closet
  Wiring from the wall jack to the patch panel should be no longer than 90 meters (plus 10 meters for patch cables)
Telecommunications Closet
  TC provides connectivity to computer equipment in the nearby work area
  Typical equipment includes patch panels to terminate horizontal wiring runs, hubs and switches
  A TC that houses the cabling and devices for work area computers is referred to as an intermediate distribution frame (IDF)
Notes: Structured Cabling: Managing and Installing a UTP Cable Plant
Horizontal wiring – runs from the work area’s wall jack to the telecommunication closet
  Wiring from the wall jack to the patch panel should be no longer than 90 meters (plus 10 meters for patch cables)
Telecommunications Closet
  TC provides connectivity to computer equipment in the nearby work area
  Typical equipment includes patch panels to terminate horizontal wiring runs, hubs and switches
  A TC that houses the cabling and devices for work area computers is referred to as an intermediate distribution frame (IDF)

## Slide 25: Structured Cabling: Managing and Installing a UTP Cable Plant
Notes: Structured Cabling: Managing and Installing a UTP Cable Plant

## Slide 26: Structured Cabling: Managing and Installing a UTP Cable Plant
Equipment Room – houses servers, routers, switches, and other major network equipment and serves as a connection point for backbone cabling
  An equipment room that’s the connection point between IDFs is called a main distribution frame (MDF)
  An MDF can be the main cross-connect for the entire network or it might serve as the connecting point for backbone cabling between buildings
    Each building often has its own MDF
Notes: Structured Cabling: Managing and Installing a UTP Cable Plant
Equipment Room – houses servers, routers, switches, and other major network equipment and serves as a connection point for backbone cabling
  An equipment room that’s the connection point between IDFs is called a main distribution frame (MDF)
  An MDF can be the main cross-connect for the entire network or it might serve as the connecting point for backbone cabling between buildings
    Each building often has its own MDF

## Slide 27: Structured Cabling: Managing and Installing a UTP Cable Plant
Backbone Cabling – interconnects IDFs and MDFs
  Runs between floors or wings of a building and between buildings
  Frequently fiber-optic cable but can also be UTP if the distance between TCs is less than 90 meters
Notes: Structured Cabling: Managing and Installing a UTP Cable Plant
Backbone Cabling – interconnects IDFs and MDFs
  Runs between floors or wings of a building and between buildings
  Frequently fiber-optic cable but can also be UTP if the distance between TCs is less than 90 meters

## Slide 28: Structured Cabling: Managing and Installing a UTP Cable Plant
Entrance Facility – the location of the cabling and equipment that connects a corporate network to a third-party telecommunications provider
  Can also serve as an equipment room and the main cross-connect for all backbone cabling
  Where a connection to a WAN is made
  Demarcation point: point where corporate LAN equipment ends and a third-party provider’s equipment and cabling begins
Notes: Structured Cabling: Managing and Installing a UTP Cable Plant
Entrance Facility – the location of the cabling and equipment that connects a corporate network to a third-party telecommunications provider
  Can also serve as an equipment room and the main cross-connect for all backbone cabling
  Where a connection to a WAN is made
  Demarcation point: point where corporate LAN equipment ends and a third-party provider’s equipment and cabling begins

## Slide 29: Installing UTP Cabling
Cable termination – putting RJ-45 plugs on the ends of cable or punching down wires into terminal blocks on a jack or patch panel
Some tools
needed:
Wire cutters
Crimping Tool
Cable Tester
Punchdown Tool
Cable Stripper
RJ-45 plugs/jacks
Notes: Installing UTP Cabling
Cable termination – putting RJ-45 plugs on the ends of cable or punching down wires into terminal blocks on a jack or patch panel
Some tools
needed:
Wire cutters
Crimping Tool
Cable Tester
Punchdown Tool
Cable Stripper
RJ-45 plugs/jacks

## Slide 30: Installing UTP Cabling
When making a cable or terminating a cable at a jack or patch panel
  It is important to get the colored wires arranged in the correct order
  There are two standards: 568A and 568B
Notes: Installing UTP Cabling
When making a cable or terminating a cable at a jack or patch panel
  It is important to get the colored wires arranged in the correct order
  There are two standards: 568A and 568B

## Slide 31: Straight-Through Versus Crossover Cable
Standard patch cables are called straight-through cables (same wiring standard on both ends)
Crossover cables – use 568A standard on one side of the cable and 568B standard on the other side
  Crosses the transmit and receive wires so that transmit on one end connects to receive on the other
  This type of cable is often needed when you connect two devices of the same type to one another
  For a 1000BaseT crossover cable, you have to cross the blue and brown pins because they’re used in 1000BaseT
Notes: Straight-Through Versus Crossover Cable
Standard patch cables are called straight-through cables (same wiring standard on both ends)
Crossover cables – use 568A standard on one side of the cable and 568B standard on the other side
  Crosses the transmit and receive wires so that transmit on one end connects to receive on the other
  This type of cable is often needed when you connect two devices of the same type to one another
  For a 1000BaseT crossover cable, you have to cross the blue and brown pins because they’re used in 1000BaseT

## Slide 32: Straight-Through Versus Crossover Cable
Notes: Straight-Through Versus Crossover Cable

## Slide 33: Medium Dependent Interface
Network devices that connect by using RJ-45 plugs over twisted-pair cabling are classified as medium dependent interface (MDI) devices or MDI crossed (MDI-X) devices
MDI devices transmit on pins 1 and 2 and receive on pins 3 and 6
  PC NICs and routers are examples
MDI-X devices receive on pins 1 and 2 and transmit on pins 3 and 6
  Hubs and switches are examples
When two switches (or any other like devices) need to be connected, you use a crossover cable so that transmit and receive wires get crossed
Notes: Medium Dependent Interface
Network devices that connect by using RJ-45 plugs over twisted-pair cabling are classified as medium dependent interface (MDI) devices or MDI crossed (MDI-X) devices
MDI devices transmit on pins 1 and 2 and receive on pins 3 and 6
  PC NICs and routers are examples
MDI-X devices receive on pins 1 and 2 and transmit on pins 3 and 6
  Hubs and switches are examples
When two switches (or any other like devices) need to be connected, you use a crossover cable so that transmit and receive wires get crossed

## Slide 34: Why Two Transmit and Two Receive Wires?
One wire pair is used for transmit (labeled transmit+/transmit-) and one pair for receive (labeled receive+/receive-)
The plus and minus symbols indicate that the wires carry a positive and negative signal
  This differential signal mitigates the effect of crosstalk and noise on the cable
Notes: Why Two Transmit and Two Receive Wires?
One wire pair is used for transmit (labeled transmit+/transmit-) and one pair for receive (labeled receive+/receive-)
The plus and minus symbols indicate that the wires carry a positive and negative signal
  This differential signal mitigates the effect of crosstalk and noise on the cable

## Slide 35: Fiber-Optic Cable
Bits are transmitted as pulses of light instead of electricity
Immune to electrical interference
Highly secure – electronic eavesdropping is eliminated
Composition
  A slender cylinder of glass fiber called the core is surrounded by a concentric layer of glass called the cladding
  Fiber is then jacketed in a thin transparent plastic material called the buffer
Notes: Fiber-Optic Cable
Bits are transmitted as pulses of light instead of electricity
Immune to electrical interference
Highly secure – electronic eavesdropping is eliminated
Composition
  A slender cylinder of glass fiber called the core is surrounded by a concentric layer of glass called the cladding
  Fiber is then jacketed in a thin transparent plastic material called the buffer

## Slide 36: Fiber-Optic Cable
Notes: Fiber-Optic Cable

## Slide 37: Fiber-Optic Cable
Each fiber-optic strand carries data in only one direction
  Network connections consist of two or more strands
Fiber-optic cable used as backbone cabling often comes in bundles of 12 or more fiber strands
  Even only using 2 in the backbone, running more is a good idea so that you are ready for any future expansion
Some testing has shown that glass fibers can carry several terabits (1000 gigabits) per second
  Fiber-optic cable may one day replace copper for all types of network connections
Notes: Fiber-Optic Cable
Each fiber-optic strand carries data in only one direction
  Network connections consist of two or more strands
Fiber-optic cable used as backbone cabling often comes in bundles of 12 or more fiber strands
  Even only using 2 in the backbone, running more is a good idea so that you are ready for any future expansion
Some testing has shown that glass fibers can carry several terabits (1000 gigabits) per second
  Fiber-optic cable may one day replace copper for all types of network connections

## Slide 38: Fiber-Optic Cable
Notes: Fiber-Optic Cable

## Slide 39: Fiber-Optic Connectors
Types of connectors:
  Straight tip (ST)
  Straight connection (SC)
  Locking connection (LC)
  Mechanical transfer registered jack (MT-RJ)
  Fiber channel or ferrule connector (FC)
  Medium interface connector (MIC)
  Subminiature type A (SMA)
Notes: Fiber-Optic Connectors
Types of connectors:
  Straight tip (ST)
  Straight connection (SC)
  Locking connection (LC)
  Mechanical transfer registered jack (MT-RJ)
  Fiber channel or ferrule connector (FC)
  Medium interface connector (MIC)
  Subminiature type A (SMA)

## Slide 40: Fiber-Optic Connectors
Notes: Fiber-Optic Connectors

## Slide 41: Fiber-Optic Installation
Somewhat more difficult and time consuming than copper media installation
  However, advances in connector technology is closing the gap
Connectors and test equipment required for termination are still more expensive than copper
There are many methods for terminating fiber-optic cables because of the many connectors and cable types available
  Installation details are beyond the scope of this book
Notes: Fiber-Optic Installation
Somewhat more difficult and time consuming than copper media installation
  However, advances in connector technology is closing the gap
Connectors and test equipment required for termination are still more expensive than copper
There are many methods for terminating fiber-optic cables because of the many connectors and cable types available
  Installation details are beyond the scope of this book

## Slide 42: Fiber-Optic Cable Types
Single-mode fiber (SMF)
  Includes a single, small-diameter fiber at the core (8 microns)
  Generally works with laser-based emitters
  Spans the longest distances
  Used in higher-bandwidth applications
Multimode fiber (MMF)
  Larger diameter fiber at the core (50 and 62.5 microns)
  Costs less than SMF
  Works with lower-power light emitting diodes (LEDs)
  Spans shorter distances
Notes: Fiber-Optic Cable Types
Single-mode fiber (SMF)
  Includes a single, small-diameter fiber at the core (8 microns)
  Generally works with laser-based emitters
  Spans the longest distances
  Used in higher-bandwidth applications
Multimode fiber (MMF)
  Larger diameter fiber at the core (50 and 62.5 microns)
  Costs less than SMF
  Works with lower-power light emitting diodes (LEDs)
  Spans shorter distances

## Slide 43: Cable-Testing Equipment
Common tools for testing and troubleshooting wired networks:
  Cable certifier
  Basic cable tester
  Tone generator
  Time domain reflectometer (TDR)
  Multimeter
  Optical power meter (OPM)
Notes: Cable-Testing Equipment
Common tools for testing and troubleshooting wired networks:
  Cable certifier
  Basic cable tester
  Tone generator
  Time domain reflectometer (TDR)
  Multimeter
  Optical power meter (OPM)

## Slide 44: Wireless Networking
Demand has increased considerably
  Many home users have turned to wireless networks
Wireless networks are often used with wired networks to interconnect geographically dispersed LANs or groups of mobile users with wired servers and resources on a wired LAN (sometimes referred to as “hybrid networks”)
Even in small networks with workstations connecting to a wireless AP or router, the AP or router usually connects to the Internet via a wired connection to a cable modem
Notes: Wireless Networking
Demand has increased considerably
  Many home users have turned to wireless networks
Wireless networks are often used with wired networks to interconnect geographically dispersed LANs or groups of mobile users with wired servers and resources on a wired LAN (sometimes referred to as “hybrid networks”)
Even in small networks with workstations connecting to a wireless AP or router, the AP or router usually connects to the Internet via a wired connection to a cable modem

## Slide 45: Wireless Benefits
Creates temporary connections to wired networks
Establishes backup or contingency connectivity for existing wired networks
Extends a network’s span beyond the reach of wire-based or fiber-optic cabling, especially in older buildings where rewiring might be too expensive
Allows businesses to provide customers with wireless networking easily, offering a service that gets customers in and keeps them there
Enables users to roam around a corporate or college campus with their machines
Notes: Wireless Benefits
Creates temporary connections to wired networks
Establishes backup or contingency connectivity for existing wired networks
Extends a network’s span beyond the reach of wire-based or fiber-optic cabling, especially in older buildings where rewiring might be too expensive
Allows businesses to provide customers with wireless networking easily, offering a service that gets customers in and keeps them there
Enables users to roam around a corporate or college campus with their machines

## Slide 46: Wireless Benefits
Notes: Wireless Benefits

## Slide 47: Types of Wireless Networks
Local area networks (LANs) – usually provides connectivity for mobile users or across areas that couldn’t otherwise be networked
Extended LANs – usually used to increase a LAN’s span beyond normal distance limitations
Internet service – used to bring Internet access to homes and businesses
Mobile computing – users communicate by using a wireless networking medium that enable them to move while remaining connected to a network
Notes: Types of Wireless NetworksLocal area networks (LANs) – usually provides connectivity for mobile users or across areas that couldn’t otherwise be networked
Extended LANs – usually used to increase a LAN’s span beyond normal distance limitations
Internet service – used to bring Internet access to homes and businesses
Mobile computing – users communicate by using a wireless networking medium that enable them to move while remaining connected to a network

## Slide 48: Wireless LAN Components
Network interface attaches to an antenna and an emitter rather than to a cable
Transceiver/access point (AP) – a transmitter/receiver device that must be installed to translate between wired and wireless networks
  Includes an antenna and a transmitter to send and receive wireless traffic but also connects to the wired side of the network
  Shuttles traffic back and forth between a network’s wired and wireless sides
Notes: Wireless LAN Components
Network interface attaches to an antenna and an emitter rather than to a cable
Transceiver/access point (AP) – a transmitter/receiver device that must be installed to translate between wired and wireless networks
  Includes an antenna and a transmitter to send and receive wireless traffic but also connects to the wired side of the network
  Shuttles traffic back and forth between a network’s wired and wireless sides

## Slide 49: Wireless LAN Transmission
Signals take the form of waves in the electromagnetic (EM) spectrum
The frequency of the wave forms used for communication is measured in cycles per second, usually expressed as hertz (Hz)
Lower-frequency transmissions can carry less data more slowly over longer distances, and higher-frequency transmissions can carry more data faster over shorter distances (high frequency radio waves has higher signaling rate)
Notes: Wireless LAN Transmission
Signals take the form of waves in the electromagnetic (EM) spectrum
The frequency of the wave forms used for communication is measured in cycles per second, usually expressed as hertz (Hz)
Lower-frequency transmissions can carry less data more slowly over longer distances, and higher-frequency transmissions can carry more data faster over shorter distances

## Slide 50: Wireless LAN Transmission
The following are the most common frequencies for wireless data communication:
  Radio – 10 KHz to 300 MHz
  Microwave – 300 MHz to 300 GHz
  Infrared – 300 GHz to 400 THz (terahertz)
Wireless LANs make use of four primary technologies for transmitting and receiving data
  Infrared
  Laser
  Narrowband (single-frequency) radio
  Spread-spectrum radio
Notes: Wireless LAN Transmission
The following are the most common frequencies for wireless data communication:
  Radio – 10 KHz to 300 MHz
  Microwave – 300 MHz to 300 GHz
  Infrared – 300 GHz to 400 THz (terahertz)
Wireless LANs make use of four primary technologies for transmitting and receiving data
  Infrared
  Laser
  Narrowband (single-frequency) radio
  Spread-spectrum radio

## Slide 51: Infrared LAN Technologies
Infrared (IR) wireless networks use infrared light beams to send signals between pairs of devices
  Works well for LAN applications due to high bandwidth
  Four main kinds of infrared LANs
    Line-of-sight networks – require an unobstructed view between transmitter and receiver
    Reflective wireless networks – broadcast signals from optical transceivers near devices to a central hub
    Scatter infrared networks – bounce transmissions off walls and ceilings to deliver signals
    Broadband optical telepoint networks – provide broadband services
Notes: Infrared LAN Technologies
Infrared (IR) wireless networks use infrared light beams to send signals between pairs of devices
  Works well for LAN applications due to high bandwidth
  Four main kinds of infrared LANs
    Line-of-sight networks – require an unobstructed view between transmitter and receiver
    Reflective wireless networks – broadcast signals from optical transceivers near devices to a central hub
    Scatter infrared networks – bounce transmissions off walls and ceilings to deliver signals
    Broadband optical telepoint networks – provide broadband services

## Slide 52: Laser-Based LAN Technologies
Also require a clear line of sight between sender and receiver
Subject to many of the same limitations as infrared
  Aren’t as susceptible to interference from visible light sources as infrared
Notes: Laser-Based LAN Technologies
Also require a clear line of sight between sender and receiver
Subject to many of the same limitations as infrared
  Aren’t as susceptible to interference from visible light sources as infrared

## Slide 53: Narrowband Radio LAN Technologies
Use low-powered, two-way radio communication
Receiver and transmitter must be tuned to the same frequency to handle incoming and outgoing data
Requires no line of sight between sender and receiver as long as both parties stay within the broadcast range of these devices
  Typically 70 meters or 230 feet
Depending on the frequency, walls or other solid barriers can block signals
Interference from other radio sources is possible
Notes: Narrowband Radio LAN Technologies
Use low-powered, two-way radio communication
Receiver and transmitter must be tuned to the same frequency to handle incoming and outgoing data
Requires no line of sight between sender and receiver as long as both parties stay within the broadcast range of these devices
  Typically 70 meters or 230 feet
Depending on the frequency, walls or other solid barriers can block signals
Interference from other radio sources is possible

## Slide 54: Narrowband Radio LAN Technologies
Notes: Narrowband Radio LAN Technologies

## Slide 55: Spread-Spectrum LAN Technologies
Uses multiple frequencies simultaneously, improving reliability and reducing susceptibility to interference
  Also makes eavesdropping more difficult
Two main kinds of spread-spectrum communications
  Frequency hopping – switches data between multiple frequencies at regular intervals
  Direct-sequence modulation – breaks data into fixed-size segments called chips and transmits the data on several different frequencies at the same time
Notes: Spread-Spectrum LAN Technologies
Uses multiple frequencies simultaneously, improving reliability and reducing susceptibility to interference
  Also makes eavesdropping more difficult
Two main kinds of spread-spectrum communications
  Frequency hopping – switches data between multiple frequencies at regular intervals
  Direct-sequence modulation – breaks data into fixed-size segments called chips and transmits the data on several different frequencies at the same time

## Slide 56: Spread-Spectrum LAN Technologies
Notes: Spread-Spectrum LAN Technologies

## Slide 57: LAN Media Selection Criteria
Three main media choices: UTP, fiber-optic, and wireless
When choosing between media types, consider:
  Bandwidth – Higher bandwidth means more expensive cable and higher installation costs
    If 40 Gbps or more, fiber-optic is the only choice
  Budget – A typical UTP cable installation cost $100 - $200 per cable run and fiber-optic might cost twice that much
    Wireless have no physical installation costs but you need to install access points and verify connectivity
Notes: LAN Media Selection Criteria
Three main media choices: UTP, fiber-optic, and wireless
When choosing between media types, consider:
  Bandwidth – Higher bandwidth means more expensive cable and higher installation costs
    If 40 Gbps or more, fiber-optic is the only choice
  Budget – A typical UTP cable installation cost $100 - $200 per cable run and fiber-optic might cost twice that much
    Wireless have no physical installation costs but you need to install access points and verify connectivity

## Slide 58: LAN Media Selection Criteria
When choosing between media types, consider:
  Environmental considerations – How electrically noisy is the environment? How important is data security?
    The more weight either factor has, the more likely fiber-optic or secured wireless is the right choice
  Span – What kind of distance must the network span?
    Longer spans might require fiber-optic or wireless be used between buildings
    Strategic placement of small switches or hubs gives UTP surprising reach
  Existing cable plant – For an upgrade, the existing cable plant must be considered
Notes: LAN Media Selection Criteria
When choosing between media types, consider:
  Environmental considerations – How electrically noisy is the environment? How important is data security?
    The more weight either factor has, the more likely fiber-optic or secured wireless is the right choice
  Span – What kind of distance must the network span?
    Longer spans might require fiber-optic or wireless be used between buildings
    Strategic placement of small switches or hubs gives UTP surprising reach
  Existing cable plant – For an upgrade, the existing cable plant must be considered

## Slide 59: LAN Media Selection Criteria
Notes: LAN Media Selection Criteria

## Slide 60: Summary
Wired networking media come in two primary categories: copper and fiber-optic
Twisted pair cabling come in shielded or unshielded varieties
Twisted pair cabling components consist of connectors, patch cable, jacks, patch panels and distribution racks
A structured cabling plant consists of work areas, horizontal wiring, telecommunications closets, equipment rooms, backbone cabling, and entrance facilities
Notes: Summary
Wired networking media come in two primary categories: copper and fiber-optic
Twisted pair cabling come in shielded or unshielded varieties
Twisted pair cabling components consist of connectors, patch cable, jacks, patch panels and distribution racks
A structured cabling plant consists of work areas, horizontal wiring, telecommunications closets, equipment rooms, backbone cabling, and entrance facilities

## Slide 61: Summary
Fiber-optic uses pulses of light to represent bits and is immune to EMI, RFI and electronic eavesdropping
Wireless networks can be subdivided into LANs, extended LANs, and mobile computing
Components of a wireless LAN are a NIC, an antenna, and a transceiver or access point
Technologies used to transmit and receive data including: infrared, laser, narrowband radio and spread-spectrum radio
Networks combining fiber-optic, UTP, and wireless have become the norm
Notes: Summary
Fiber-optic uses pulses of light to represent bits and is immune to EMI, RFI and electronic eavesdropping
Wireless networks can be subdivided into LANs, extended LANs, and mobile computing
Components of a wireless LAN are a NIC, an antenna, and a transceiver or access point
Technologies used to transmit and receive data including: infrared, laser, narrowband radio and spread-spectrum radio
Networks combining fiber-optic, UTP, and wireless have become the norm
longer distances in two or more geographical areas