## Slide 1: Guide to Networking Essentials, 7th ed.
Topic 05
Troubleshooting and Support
Notes: Guide to Networking Essentials, 7th ed.
Chapter 13: Troubleshooting and Support

## Slide 2: Objectives
2
Describe the benefits of documenting a network and list what elements should be documented
List the steps of the problem-solving process
Explain different approaches to network troubleshooting
Make use of problem-solving resources
Describe network troubleshooting tools
Summarize common trouble situations
Describe disaster recovery procedures
Notes: Objectives
Describe the benefits of documenting a network and list what elements should be documented
List the steps of the problem-solving process
Explain different approaches to network troubleshooting
Make use of problem-solving resources
Describe network troubleshooting tools
Summarize common trouble situations
Describe disaster recovery procedures

## Slide 3: Documenting Your Network
Why should you document your network?
  Makes equipment moves, adds and changes easier
  Provides needed information for troubleshooting
  Offers justification for additional staff or equipment
  Helps determine compliance with standards
  Supplies proof that your installations meet hardware or software requirements
  Reduces training requirements
  Facilitates security management
  Improves compliance with software licensing agreements
Notes: Documenting Your Network
Why should you document your network?
  Makes equipment moves, adds and changes easier
  Provides needed information for troubleshooting
  Offers justification for additional staff or equipment
  Helps determine compliance with standards
  Supplies proof that your installations meet hardware or software requirements
  Reduces training requirements
  Facilitates security management
  Improves compliance with software licensing agreements

## Slide 4: Change Management
When a workstation is moved, you must know which patch-panel and switch ports are currently being used so they can be disconnected
Without proper documentation, cables must be traced
Additions made to your network can happen more quickly and with less chance for errors if documentation is up to date
Change management – document reasons for change, the potential impact of a change, notifications, and approval procedures
Notes: Change Management
When a workstation is moved, you must know which patch-panel and switch ports are currently being used so they can be disconnected
Without proper documentation, cables must be traced
Additions made to your network can happen more quickly and with less chance for errors if documentation is up to date
Change management – document reasons for change, the potential impact of a change, notifications, and approval procedures

## Slide 5: Documentation and Troubleshooting
Accurate documentation of workstation MAC addresses helps quickly find issues such as IP address conflicts and the source of invalid or excessive frames
Physical and logical addressing, connectivity to devices, and even data about the cabling should be documented
Notes: Documentation and Troubleshooting
Accurate documentation of workstation MAC addresses helps quickly find issues such as IP address conflicts and the source of invalid or excessive frames
Physical and logical addressing, connectivity to devices, and even data about the cabling should be documented

## Slide 6: Documentation and IT Staffing
Documenting the type and frequency of support calls can provide justification for additions to staff or tools to make support more efficient
Statistics on network response time and bandwidth load as justification for upgrading servers or adding new equipment
Train new employees on how to properly document additions and changes
Notes: Documentation and IT Staffing
Documenting the type and frequency of support calls can provide justification for additions to staff or tools to make support more efficient
Statistics on network response time and bandwidth load as justification for upgrading servers or adding new equipment
Train new employees on how to properly document additions and changes

## Slide 7: Documentation and Standards Compliance
Be sure to document which standards are in use
  Example: Whether 568-A or 568-B wiring standard is used for patch panels and jacks
Another reason to document standards compliance:
  When there’s a dispute between you and an equipment vendor about a persistent network error
Notes: Documentation and Standards Compliance
Be sure to document which standards are in use
  Example: Whether 568-A or 568-B wiring standard is used for patch panels and jacks
Another reason to document standards compliance:
  When there’s a dispute between you and an equipment vendor about a persistent network error

## Slide 8: Documentation and Technical Support
When solving a network device problem, some manufacturers of network devices will want to know that your cabling passed appropriate tests as well as other test results
When calling technical support for a software problem on one of your servers, the manufacturer will most likely want to know the hardware details as well as operating system version and patch installations
Notes: Documentation and Technical Support
When solving a network device problem, some manufacturers of network devices will want to know that your cabling passed appropriate tests as well as other test results
When calling technical support for a software problem on one of your servers, the manufacturer will most likely want to know the hardware details as well as operating system version and patch installations

## Slide 9: Documentation and Security
Documenting security patches and virus protection updates helps you adhere to your security policies and confirms your resistance to current threats
Notes: Documentation and Security
Documenting security patches and virus protection updates helps you adhere to your security policies and confirms your resistance to current threats

## Slide 10: What Should Be Documented?
Some items you might want to document:
  Description of the network – should include network topology, network technologies in use, the operating systems installed, and the number of devices and users served
  Cable plant – describes the physical layout of your network cabling, the terminations used, conventions used for labeling your cable and equipment, and results of test completed on the cable plant
  Equipment rooms/telecommunications closets – document the items in each room and their location
Notes: What Should Be Documented?
Some items you might want to document:
  Description of the network – should include network topology, network technologies in use, the operating systems installed, and the number of devices and users served
  Cable plant – describes the physical layout of your network cabling, the terminations used, conventions used for labeling your cable and equipment, and results of test completed on the cable plant
  Equipment rooms/telecommunications closets – document the items in each room and their location

## Slide 11: What Should Be Documented?
Some items you might want to document (cont’d):
  Internetworking devices – Know what devices are connected to other devices, network management features, port usage, physical and logical addresses, model numbers, and hardware/software revision numbers
  Servers – Document hardware configuration, operating system and application version numbers, NIC information, and system serial and model numbers
  Workstations – Hardware and software configuration, physical and logical addresses
Notes: What Should Be Documented?
Some items you might want to document (cont’d):
  Internetworking devices – Know what devices are connected to other devices, network management features, port usage, physical and logical addresses, model numbers, and hardware/software revision numbers
  Servers – Document hardware configuration, operating system and application version numbers, NIC information, and system serial and model numbers
  Workstations – Hardware and software configuration, physical and logical addresses

## Slide 12: The Problem-Solving Process
Steps of the problem-solving process:
  Determine the problem definition and scope
  Gather information
  Consider possible causes
  Devise a solution
  Implement the solution
  Test the solution
  Document the solution
  Devise preventative measures
Notes: The Problem-Solving Process
Steps of the problem-solving process:
  Determine the problem definition and scope
  Gather information
  Consider possible causes
  Devise a solution
  Implement the solution
  Test the solution
  Document the solution
  Devise preventative measures

## Slide 13: Step 1: Determine the Problem Definition and Scope
A problem definition should describe what does work and what doesn’t work
Know who and what are affected by the problem
Questions to ask:
  Is anyone else near you having the same problem?
  What about other areas of the building?
  Is the problem occurring with all applications or just one?
  If you move to a different computer, does the problem occur there as well?
Notes: Step 1: Determine the Problem Definition and Scope
A problem definition should describe what does work and what doesn’t work
Know who and what are affected by the problem
Questions to ask:
  Is anyone else near you having the same problem?
  What about other areas of the building?
  Is the problem occurring with all applications or just one?
  If you move to a different computer, does the problem occur there as well?

## Slide 14: Step 1: Determine the Problem Definition and Scope
Examples of a problem definition and scope:
  Mike can’t access the e-mail server. Other servers are available to Mike, and no one else reports the problem.
  Third-floor users can’t log on to the network, other floors can.
  Camille can’t print to the new LaserJet printer on her fourth floor. She as tried several applications. No other users have tried to print to this printer.
  Julie reports that the network is slow while accessing her Documents folder. Access to the Internet and other resources seem to work with normal performance
Assign a priority to the problem once you have defined it.
Notes: Step 1: Determine the Problem Definition and Scope
Examples of a problem definition and scope:
  Mike can’t access the e-mail server. Other servers are available to Mike, and no one else reports the problem.
  Third-floor users can’t log on to the network, other floors can.
  Camille can’t print to the new LaserJet printer on her fourth floor. She as tried several applications. No other users have tried to print to this printer.
  Julie reports that the network is slow while accessing her Documents folder. Access to the Internet and other resources seem to work with normal performance
Assign a priority to the problem once you have defined it.

## Slide 15: Step 2: Gather Information
Know the right questions to ask:
Did it ever work?
  This question is often overlooked but may prove helpful
When did it stop working?
  Does the problem occur all the time or only intermittently?
  Are there particular times of the day when the problem occurs?
  Are other applications running when the problem occurs?
Has anything changed?
  Ask your self that question as well…were any network changes made?
Notes: Step 2: Gather Information
Know the right questions to ask:
Did it ever work?
  This question is often overlooked but may prove helpful
When did it stop working?
  Does the problem occur all the time or only intermittently?
  Are there particular times of the day when the problem occurs?
  Are other applications running when the problem occurs?
Has anything changed?
  Ask your self that question as well…were any network changes made?

## Slide 16: Step 2: Gather Information
Never ignore the obvious
  Check for unplugged cables
Define how it is supposed to work
  Have good documentation and a clear baseline of your network
  A baseline of your network should include network utilization statistics; utilization statistics on server CPUs, memory, hard drives, and other resources; and normal traffic patterns
  Why important? Example – If network utilization increases 2-3% per month for several months, you can prepare for a performance upgrade
Notes: Step 2: Gather Information
Never ignore the obvious
  Check for unplugged cables
Define how it is supposed to work
  Have good documentation and a clear baseline of your network
  A baseline of your network should include network utilization statistics; utilization statistics on server CPUs, memory, hard drives, and other resources; and normal traffic patterns
  Why important? Example – If network utilization increases 2-3% per month for several months, you can prepare for a performance upgrade

## Slide 17: Step 3: Consider Possible Causes
Your goal is to create a checklist of possible things that could have gone wrong
Example: An entire area of a building lost connection with the network, but no other areas are affected
  The connection in the main wiring closet to the rest of the network has failed
  The switch to which all workstations are connected has lost power or completely failed in some way
  All workstations have acquired a virus through the network, and the virus affects their network connection
  A major upgrade has been made recently on all workstations in that area, and incorrect network addresses were configured
Notes: Step 3: Consider Possible Causes
Your goal is to create a checklist of possible things that could have gone wrong
Example: An entire area of a building lost connection with the network, but no other areas are affected
  The connection in the main wiring closet to the rest of the network has failed
  The switch to which all workstations are connected has lost power or completely failed in some way
  All workstations have acquired a virus through the network, and the virus affects their network connection
  A major upgrade has been made recently on all workstations in that area, and incorrect network addresses were configured

## Slide 18: Step 4: Devise a Solution
Before devising a solution, consider the following:
  Is the identified cause of the problem truly the cause, or is it just another symptom of the problem’s true cause?
  Is there a way to test the proposed solution adequately?
  What results should the proposed solution produce?
  What are the ramifications of the proposed solution for the rest of the network?
  Do you need additional help to answer some of these questions?
Notes: Step 4: Devise a Solution
Before devising a solution, consider the following:
  Is the identified cause of the problem truly the cause, or is it just another symptom of the problem’s true cause?
  Is there a way to test the proposed solution adequately?
  What results should the proposed solution produce?
  What are the ramifications of the proposed solution for the rest of the network?
  Do you need additional help to answer some of these questions?

## Slide 19: Step 4: Devise a Solution
You might need to:
  Save all network device configuration files
  Document and back up workstation configurations
  Document wiring closet configurations
  Conduct a final baseline to compare new and old results
Notes: Step 4: Devise a Solution
You might need to:
  Save all network device configuration files
  Document and back up workstation configurations
  Document wiring closet configurations
  Conduct a final baseline to compare new and old results

## Slide 20: Step 5: Implement the Solution
Create Intermediate Testing Opportunities
  Testing small steps in which a limited number of things could go wrong is easier than testing a complex solution with lots of problem areas
Inform Your Users
  Inform your users of the possible disruption to some network services
Put the Plan into Action
  Take notes about every change you make to the network or servers
Notes: Step 5: Implement the Solution
Create Intermediate Testing Opportunities
  Testing small steps in which a limited number of things could go wrong is easier than testing a complex solution with lots of problem areas
Inform Your Users
  Inform your users of the possible disruption to some network services
Put the Plan into Action
  Take notes about every change you make to the network or servers

## Slide 21: Step 6: Test the Solution
Your testing should attempt to emulate a real-world situation as closely as possible
If testing a workstation problem:
  Attempt to logon to the network as a user with similar privileges as the main user
  Next, attempt to access applications that would be run from that workstation
Notes: Step 6: Test the Solution
Your testing should attempt to emulate a real-world situation as closely as possible
If testing a workstation problem:
  Attempt to logon to the network as a user with similar privileges as the main user
  Next, attempt to access applications that would be run from that workstation

## Slide 22: Step 6: Test the Solution
If testing a network upgrade:
  Start some workstations on the upgraded part of the network and run some network-intensive applications
  Gather information about how the network behaves and compare to previous results (before the upgrade)
Notes: Step 6: Test the Solution
If testing a network upgrade:
  Start some workstations on the upgraded part of the network and run some network-intensive applications
  Gather information about how the network behaves and compare to previous results (before the upgrade)

## Slide 23: Step 7: Document the Solution
Your documentation should include everything pertinent to the problem
  Problem definition
  Solution
  Implementation
  Testing
If the problem and its solution have implications for the entire network, include this information
Notes: Step 7: Document the Solution
Your documentation should include everything pertinent to the problem
  Problem definition
  Solution
  Implementation
  Testing
If the problem and its solution have implications for the entire network, include this information

## Slide 24: Step 8: Devise Preventive Measures
After solving a problem, do everything you can to prevent this problem or similar problems from recurring
Example:
  If your problem was a virus that spread throughout the network, install malware protection programs on your network and tighten policies for software and e-mail downloads
Devising preventive measures is proactive rather than reactive network management
Notes: Step 8: Devise Preventive Measures
After solving a problem, do everything you can to prevent this problem or similar problems from recurring
Example:
  If your problem was a virus that spread throughout the network, install malware protection programs on your network and tighten policies for software and e-mail downloads
Devising preventive measures is proactive rather than reactive network management

## Slide 25: Approaches to Network Troubleshooting
Different methods of troubleshooting:
  Trial and Error
  Solve by Example
  The Replacement Method
  Step by Step with the OSI Model
Notes: Approaches to Network Troubleshooting
Different methods of troubleshooting:
  Trial and Error
  Solve by Example
  The Replacement Method
  Step by Step with the OSI Model

## Slide 26: Trial and Error
Trial-and-error requires an assessment of the problem, an educated guess to a solution and a test of the results
Used under the following conditions:
  The system is being newly configured, no data can be lost
  The system is not attached to a live network
  You can undo changes easily
  Other approaches would take more time than a few trial-and-error attempts
Notes: Trial and Error
Trial-and-error requires an assessment of the problem, an educated guess to a solution and a test of the results
Used under the following conditions:
  The system is being newly configured, no data can be lost
  The system is not attached to a live network
  You can undo changes easily
  Other approaches would take more time than a few trial-and-error attempts

## Slide 27: Trial and Error
Used under the following conditions (cont’d):
  There are few possible causes of the problem
  No documentation and other resources are available to draw on to arrive at a solution more scientifically
Is NOT advisable under these conditions:
  A server or internetworking device is live on the network
  The problem is being discussed over the phone and you’re instructing an untrained user
Notes: Trial and Error
Used under the following conditions (cont’d):
  There are few possible causes of the problem
  No documentation and other resources are available to draw on to arrive at a solution more scientifically
Is NOT advisable under these conditions:
  A server or internetworking device is live on the network
  The problem is being discussed over the phone and you’re instructing an untrained user

## Slide 28: Trial and Error
Is NOT advisable under these conditions (cont’d):
  You aren’t sure of the consequences of the solutions you propose
  You have no sure way to undo the changes after they’re made
  Other approaches will take the same amount of time
Notes: Trial and Error
Is NOT advisable under these conditions (cont’d):
  You aren’t sure of the consequences of the solutions you propose
  You have no sure way to undo the changes after they’re made
  Other approaches will take the same amount of time

## Slide 29: Trial and Error
Follow these guidelines when using this method:
  Make only one change at a time before testing the results
  Avoid making changes that might affect the operation of a live network
  Document the original settings of hardware and software before making changes
  Avoid making a change that can destroy user data
  If possible, avoid making a change that you can’t undo
Notes: Trial and Error
Follow these guidelines when using this method:
  Make only one change at a time before testing the results
  Avoid making changes that might affect the operation of a live network
  Document the original settings of hardware and software before making changes
  Avoid making a change that can destroy user data
  If possible, avoid making a change that you can’t undo

## Slide 30: Solve by Example
Solve by example is the process of comparing something that doesn’t work with something that does
  One of the easiest/fastest ways to solve a problem
General rules to follow:
  Use the solve-by-example approach only when the working sample has a similar environment as the problem machine
Notes: Solve by Example
Solve by example is the process of comparing something that doesn’t work with something that does
  One of the easiest/fastest ways to solve a problem
General rules to follow:
  Use the solve-by-example approach only when the working sample has a similar environment as the problem machine

## Slide 31: Solve by Example
General rules to follow (cont’d):
  Don’t make configuration changes that will cause conflicts – Don’t change the TCP/IP address of a nonworking machine to the same address as a working machine
  Don’t make any changes that could destroy data that can’t be restored
Notes: Solve by Example
General rules to follow (cont’d):
  Don’t make configuration changes that will cause conflicts – Don’t change the TCP/IP address of a nonworking machine to the same address as a working machine
  Don’t make any changes that could destroy data that can’t be restored

## Slide 32: The Replacement Method
Requires narrowing down possible sources of the problem and having known working replacement parts on hand so that they can be swapped out
Follow these rules when using this method:
  Narrow the list of potentially defective parts down to a few possibilities
  Make sure you have the correct replacement parts on hand
  Replace only one part at a time
  If your first replacement does not fix the problem, reinstall original part before replacing another part
Notes: The Replacement Method
Requires narrowing down possible sources of the problem and having known working replacement parts on hand so that they can be swapped out
Follow these rules when using this method:
  Narrow the list of potentially defective parts down to a few possibilities
  Make sure you have the correct replacement parts on hand
  Replace only one part at a time
  If your first replacement does not fix the problem, reinstall original part before replacing another part

## Slide 33: Step by Step with the OSI Model
You test a problem starting at the Application layer and keep testing at each layer until you have a successful test or reach the Physical layer
  You could also start at the Physical layer and work your way up
To use this approach, you must understand how networks work and where you should use troubleshooting tools
Notes: Step by Step with the OSI Model
You test a problem starting at the Application layer and keep testing at each layer until you have a successful test or reach the Physical layer
  You could also start at the Physical layer and work your way up
To use this approach, you must understand how networks work and where you should use troubleshooting tools

## Slide 34: Making Use of Problem-Solving Resources
Resources available to you during the troubleshooting process:
  Experience
  The Internet
  Network Documentation
Notes: Making Use of Problem-Solving Resources
Resources available to you during the troubleshooting process:
  Experience
  The Internet
  Network Documentation

## Slide 35: Experience
Make the most of your experience
  Take notes about what you see and learn
If it happened once, it will happen again
  Don’t think that a problem is so obscure that it will never happen again – take the time to make not of it
Colleagues’ experience
  Use the people you know as a resource
Notes: Experience
Make the most of your experience
  Take notes about what you see and learn
If it happened once, it will happen again
  Don’t think that a problem is so obscure that it will never happen again – take the time to make not of it
Colleagues’ experience
  Use the people you know as a resource

## Slide 36: Experience
Experience from Manufacturer’s Technical Support
  Best time to call is when you have a specific error number or message that you can report to the manufacturer
  Have software version numbers or hardware’s serial number available when calling
Notes: Experience
Experience from Manufacturer’s Technical Support
  Best time to call is when you have a specific error number or message that you can report to the manufacturer
  Have software version numbers or hardware’s serial number available when calling

## Slide 37: The Internet
Most manufacturers create databases of problems and solutions so their customers can research the problem themselves (called a knowledge base or frequently asked questions/FAQ document)
Using a Knowledge Base or Search Engine
  Be as specific as possible
  With error messages, enclose them in quotations marks
Notes: The Internet
Most manufacturers create databases of problems and solutions so their customers can research the problem themselves (called a knowledge base or frequently asked questions/FAQ document)
Using a Knowledge Base or Search Engine
  Be as specific as possible
  With error messages, enclose them in quotations marks

## Slide 38: The Internet
Finding Drivers and Updates
  When installing a new device or OS, check whether bug fixes, driver updates, or new firmware revisions are available
Consulting Online Support Services and Newsgroups
  Many online support services are dedicated to technical subjects
  A useful subscription pay service is Experts Exchange (www.experts-exchange.com)
Notes: The Internet
Finding Drivers and Updates
  When installing a new device or OS, check whether bug fixes, driver updates, or new firmware revisions are available
Consulting Online Support Services and Newsgroups
  Many online support services are dedicated to technical subjects
  A useful subscription pay service is Experts Exchange (www.experts-exchange.com)

## Slide 39: The Internet
Researching Online Periodicals
  Some of the most popular networking journals include:
    Network Computing
    Information Week
    Network World
    Windows IT Pro Magazine
    Linux Journal
Notes: The Internet
Researching Online Periodicals
  Some of the most popular networking journals include:
    Network Computing
    Information Week
    Network World
    Windows IT Pro Magazine
    Linux Journal

## Slide 40: Network Documentation
Your documentation should read like a user’s manual for network administrators
Network Diagrams
  Include network diagrams showing a logical picture of the network and another diagram showing the network’s physical aspects (rooms, devices, and connections)
Notes: Network Documentation
Your documentation should read like a user’s manual for network administrators
Network Diagrams
  Include network diagrams showing a logical picture of the network and another diagram showing the network’s physical aspects (rooms, devices, and connections)

## Slide 41: Network Documentation
Notes: Network Documentation

## Slide 42: Network Documentation
Notes: Network Documentation

## Slide 43: Network Documentation
Internetworking Devices
  Require different levels of documentation
    Simple, unmanaged switches require the least information
  Should include model and serial numbers, location, IP address, MAC address and # of Ports (total and number of free ports)
Notes: Network D
Internetworking Devices
  Require different levels of documentation
    Simple, unmanaged switches require the least information
  Should include model and serial numbers, location, IP address, MAC address and # of Ports (total and number of free ports)
ocumentation

## Slide 44: Network Troubleshooting Tools
Common tools for troubleshooting a network:
  Ping and Trace Route
  Network Monitors
  Protocol Analyzers
  Time-Domain Reflectometer (TDR)
  Cable Testers
  Additional Tools
Notes: Network Troubleshooting Tools
Common tools for troubleshooting a network:
  Ping and Trace Route
  Network Monitors
  Protocol Analyzers
  Time-Domain Reflectometer (TDR)
  Cable Testers
  Additional Tools

## Slide 45: Using ping and tracert
The ping command tells you whether your computer can communicate with another computer using IP
  With a successful reply, you know that the target machine is running and there is a path between your computer and the target
  Also tells you the amount of time elapsed before a reply was received
With a connectivity problem, first verify that there are link lights on the switch and/or NIC
  Next, you can use ping to verify Network layer connectivity
Notes: Using ping and tracert
The ping command tells you whether your computer can communicate with another computer using IP
  With a successful reply, you know that the target machine is running and there is a path between your computer and the target
  Also tells you the amount of time elapsed before a reply was received
With a connectivity problem, first verify that there are link lights on the switch and/or NIC
  Next, you can use ping to verify Network layer connectivity

## Slide 46: Using ping and tracert
Follow these steps:
  Run ipconfig/all – this displays IP configuration
  Ping loopback address – if you ping 127.0.0.1 and receive a successful response, you have verified the IP protocol is working properly
  Ping local IP address – verifies that the computer can receive ICMP packets
  Ping default gateway – default gateway is the address of the router the computer sends packets to when the destination is on another network
  Ping IP address of host – verifies if you can communicate using ICMP of the target computer
  Ping the hostname – verifies you can resolve the hostname
Notes: Using ping and tracert
Follow these steps:
  Run ipconfig/all – this displays IP configuration
  Ping loopback address – if you ping 127.0.0.1 and receive a successful response, you have verified the IP protocol is working properly
  Ping local IP address – verifies that the computer can receive ICMP packets
  Ping default gateway – default gateway is the address of the router the computer sends packets to when the destination is on another network
  Ping IP address of host – verifies if you can communicate using ICMP of the target computer
  Ping the hostname – verifies you can resolve the hostname

## Slide 47: Using ping and tracert
Follow these steps (continued):
  Ping DNS servers – a response from DNS servers indicates your computer can communicate with a server that can resolve names to IP addresses
  Use Nslookup – to verify that the DNS server can resolve the name of the host you’re trying to communicate with
Using tracert
  tracert does a reverse DNS lookup on the IP address of each router and displays the name of the router
  Response times can help you determine if there is a bottleneck between the source and destination
  Can also be used to confirm your network design
Notes: Using ping and tracert
Follow these steps (continued):
  Ping DNS servers – a response from DNS servers indicates your computer can communicate with a server that can resolve names to IP addresses
  Use Nslookup – to verify that the DNS server can resolve the name of the host you’re trying to communicate with
Using tracert
  tracert does a reverse DNS lookup on the IP address of each router and displays the name of the router
  Response times can help you determine if there is a bottleneck between the source and destination
  Can also be used to confirm your network design

## Slide 48: Ping and Trace Route
Notes: Ping and Trace Route

## Slide 49: Network Monitors
Network monitors are software packages that can track all or part of the network traffic
  Can track packet type, errors, and traffic to and from each computer
  Can generate reports and graphs
  Some programs can email administrators when a problem is detected
Notes: Network Monitors
Network monitors are software packages that can track all or part of the network traffic
  Can track packet type, errors, and traffic to and from each computer
  Can generate reports and graphs
  Some programs can email administrators when a problem is detected

## Slide 50: Protocol Analyzers
A protocol analyzer allows you to capture packets and analyze the network traffic generated by different protocols
  Can be used to troubleshoot problems related to DNS, authentication, DHCP, IP addressing, remote access, etc…
  Also used to create baselines for network performance
Most advanced analyzers combine hardware and software in a self-contained unit
  Examples: Savvius (WildPackets) OmniPeek, Fluke Network OptiView Network Analyzer, Wireshark
Notes: Protocol Analyzers
A protocol analyzer allows you to capture packets and analyze the network traffic generated by different protocols
  Can be used to troubleshoot problems related to DNS, authentication, DHCP, IP addressing, remote access, etc…
  Also used to create baselines for network performance
Most advanced analyzers combine hardware and software in a self-contained unit
  Examples: Savvius (WildPackets) OmniPeek, Fluke Network OptiView Network Analyzer, Wireshark

## Slide 51: Time-Domain Reflectometer (TDR)
Used to determine whether there is a break or short in a cable and measure the cable’s length
The TDR sends an electrical pulse down the cable that reflects back when it encounters a break or short
  It measures the time it takes for the signal to return and can estimate how far down the cable the fault is located
You should use a TDR to document actual lengths of all cables
Notes: Time-Domain Reflectometer (TDR)
Used to determine whether there is a break or short in a cable and measure the cable’s length
The TDR sends an electrical pulse down the cable that reflects back when it encounters a break or short
  It measures the time it takes for the signal to return and can estimate how far down the cable the fault is located
You should use a TDR to document actual lengths of all cables

## Slide 52: Basic Cable Testers
Usually cost less than $100
Only test the correct termination of a twisted-pair cable or the continuity of a coaxial cable
Great for checking patch cables and testing correct termination at the patch panel and jack
Cannot check for attenuation, noise or other possible performance problems
Notes: Basic Cable Testers
Usually cost less than $100
Only test the correct termination of a twisted-pair cable or the continuity of a coaxial cable
Great for checking patch cables and testing correct termination at the patch panel and jack
Cannot check for attenuation, noise or other possible performance problems

## Slide 53: Advanced Cable Testers
More expensive than TDRs or basic cable testers
Performs several test for crosstalk, attenuation, EMI, and impedance mismatches
Some advanced cable testers can measure frame counts, collisions, CRC errors, and broadcast storms
Can cost from $1000 to several thousand dollars
Notes: Advanced Cable Testers
More expensive than TDRs or basic cable testers
Performs several test for crosstalk, attenuation, EMI, and impedance mismatches
Some advanced cable testers can measure frame counts, collisions, CRC errors, and broadcast storms
Can cost from $1000 to several thousand dollars

## Slide 54: Additional Tools
Multimeter – can measure voltage, current, and resistance on a wire
  Resistance (impedance) measures the opposition to electrical current and is important in determining faults
Tone generator and probe – generator issues an electrical signal and a probe (tone locator) detects the signal and emits a tone
  Useful for locating a wire that might be in a bundle of other wires
Notes: Additional Tools
Multimeter – can measure voltage, current, and resistance on a wire
  Resistance (impedance) measures the opposition to electrical current and is important in determining faults
Tone generator and probe – generator issues an electrical signal and a probe (tone locator) detects the signal and emits a tone
  Useful for locating a wire that might be in a bundle of other wires

## Slide 55: Additional Tools
Optical power meter (OPM) – used to measure the amount of light on a fiber-optic circuit
  Often used to determine the amount of signal loss on a fiber-optic cable between the transmitter (emitter) and receiver
  Amount of signal loss can determine whether the fiber-optic cable termination was done correctly and whether the receiver can interpret signals correctly
Notes: Additional Tools
Optical power meter (OPM) – used to measure the amount of light on a fiber-optic circuit
  Often used to determine the amount of signal loss on a fiber-optic cable between the transmitter (emitter) and receiver
  Amount of signal loss can determine whether the fiber-optic cable termination was done correctly and whether the receiver can interpret signals correctly

## Slide 56: Common Troubleshooting Situations
Cabling and Related Components
  First step is to determine whether the problem is with the cable or computer – check by connecting another computer to the cable
  Verify it is the right type of cable for the connection and that it is terminated correctly
  Check the back of the NIC card to see if it has indicator lights
  If NIC has no lights, you can try swapping out NICs
Notes: Common Troubleshooting Situations
Cabling and Related Components
  First step is to determine whether the problem is with the cable or computer – check by connecting another computer to the cable
  Verify it is the right type of cable for the connection and that it is terminated correctly
  Check the back of the NIC card to see if it has indicator lights
  If NIC has no lights, you can try swapping out NICs

## Slide 57: Common Troubleshooting Situations
Power Fluctuations
  Verify that the servers are up and running
  Use UPSs with battery power to they can be shut down without data loss (in the event of power loss)
Upgrades - when you perform network upgrades:
    Keep current and do one upgrade at a time to make your life easier
    Test any upgrade before deploying it on your production network
    Tell users about upgrades – they will be more understanding if they are notified beforehand
Notes: Common Troubleshooting Situations
Power Fluctuations
  Verify that the servers are up and running
  Use UPSs with battery power to they can be shut down without data loss (in the event of power loss)
Upgrades - when you perform network upgrades:
    Keep current and do one upgrade at a time to make your life easier
    Test any upgrade before deploying it on your production network
    Tell users about upgrades – they will be more understanding if they are notified beforehand

## Slide 58: Common Troubleshooting Situations
Poor Network Performance
  What has changed since the last time the network functioned normally?
  Has new equipment been added to the network?
  Have new applications been added to computers on the network?
  Is someone playing electronic games across the network?
  Are there new users on the network? How many?
  Could any other new equipment, such as a generator, cause interference near the network?
If new users, added equipment, or newly introduced applications degrade network performance, time to expand your network
Notes: Common Troubleshooting Situations
Poor Network Performance
  What has changed since the last time the network functioned normally?
  Has new equipment been added to the network?
  Have new applications been added to computers on the network?
  Is someone playing electronic games across the network?
  Are there new users on the network? How many?
  Could any other new equipment, such as a generator, cause interference near the network?
If new users, added equipment, or newly introduced applications degrade network performance, time to expand your network

## Slide 59: Disaster Recovery
Disaster can be anything from a server disk crash to a fire or flood
This section focuses on:
  Backup procedures
  Recovery from system failure
Notes: Disaster Recovery
Disaster can be anything from a server disk crash to a fire or flood
This section focuses on:
  Backup procedures
  Recovery from system failure

## Slide 60: Backing Up Network Data
Determine what data should be backed up and how often
Develop a schedule for backing up your data
Identify people responsible for performing backups
Test your backup system regularly
Maintain a backup log listing what data was back up, when the backup took place, who performed the backup, and what media was used
Develop a plan for storing data after it has been backed up
Notes: Backing Up Network Data
Determine what data should be backed up and how often
Develop a schedule for backing up your data
Identify people responsible for performing backups
Test your backup system regularly
Maintain a backup log listing what data was back up, when the backup took place, who performed the backup, and what media was used
Develop a plan for storing data after it has been backed up

## Slide 61: Backup Types
Full backup – copies all selected files to the selected media and marks files as backed up
Incremental backup – copies all files changed since the last full or incremental backup and marks files as backed up
Differential backup – copies all files since the last file backup; doesn’t mark files as backed up
Copy backup – copies selected files to the selected media without marking files as backed up
Notes: Backup Types
Full backup – copies all selected files to the selected media and marks files as backed up
Incremental backup – copies all files changed since the last full or incremental backup and marks files as backed up
Differential backup – copies all files since the last file backup; doesn’t mark files as backed up
Copy backup – copies selected files to the selected media without marking files as backed up

## Slide 62: Backup Types
Daily backup – copies all files changed the day the backup is made; doesn’t mark files as backed up
Bare metal restore backup – designed to allow restoring the system disk directly from backup media without having to install the OS and backup software first
Of these backup types:
  Full, incremental, and differential backups are most useful as part of a regular backup schedule
Notes: Backup Types
Daily backup – copies all files changed the day the backup is made; doesn’t mark files as backed up
Bare metal restore backup – designed to allow restoring the system disk directly from backup media without having to install the OS and backup software first
Of these backup types:
  Full, incremental, and differential backups are most useful as part of a regular backup schedule

## Slide 63: Backup Types
A good model for creating a backup schedule combines a weekly full backup with daily differential backups
When creating a schedule, post the schedule and assign one person to perform the backups and sign off on them
Windows systems have an additional backup type called a system state backup
  Copies the boot files, registry, Active Directory on domain controllers, and other critical information
Notes: Backup Types
A good model for creating a backup schedule combines a weekly full backup with daily differential backups
When creating a schedule, post the schedule and assign one person to perform the backups and sign off on them
Windows systems have an additional backup type called a system state backup
  Copies the boot files, registry, Active Directory on domain controllers, and other critical information

## Slide 64: Business Continuity
Business continuity consists of the policies, procedures, and resources required to ensure a business can function after a major catastrophe
If the bulk of IT infrastructure is maintained in house, the company should consider one of the following options:
  Cold site – physical location that house the hardware needed to get IT functioning again
  Warm site – location containing all infrastructure needed for operations to continue
  Hot site – can be running at a moment’s notice
Notes: Business Continuity
Business continuity consists of the policies, procedures, and resources required to ensure a business can function after a major catastrophe
If the bulk of IT infrastructure is maintained in house, the company should consider one of the following options:
  Cold site – physical location that house the hardware needed to get IT functioning again
  Warm site – location containing all infrastructure needed for operations to continue
  Hot site – can be running at a moment’s notice

## Slide 65: Chapter Summary
Documenting a network can provide the following advantages:
  Makes moves, adds and changes easier, provides needed information for troubleshooting, offers justification for additional staff or equipment, helps determine compliance with standards, supplies proof that your installations meet manufacturer hardware or software requirements, reduces training requirements, facilitates security management, allows for better compliance with software licensing agreements
Notes: Chapter Summary
Documenting a network can provide the following advantages:
  Makes moves, adds and changes easier, provides needed information for troubleshooting, offers justification for additional staff or equipment, helps determine compliance with standards, supplies proof that your installations meet manufacturer hardware or software requirements, reduces training requirements, facilitates security management, allows for better compliance with software licensing agreements

## Slide 66: Chapter Summary
Elements of the network that should be documented include:
  A network description, the cable plant, equipment rooms, internetworking devices, servers and workstations
The problem solving process involves eight steps:
  Determine the problem definition and scope, gather information, consider possible causes, devise a solution, implement the solution, test the solution, document the solution, and devise preventive measures
Notes: Chapter Summary
Elements of the network that should be documented include:
  A network description, the cable plant, equipment rooms, internetworking devices, servers and workstations
The problem solving process involves eight steps:
  Determine the problem definition and scope, gather information, consider possible causes, devise a solution, implement the solution, test the solution, document the solution, and devise preventive measures

## Slide 67: Chapter Summary
There are many approaches to network troubleshooting including:
  Trial and error, solve by example, the replacement method, and step by step using the OSI model
Resources available to help troubleshoot include experience, the Web, and network documentation
There are several tools you can use to get information from your network and its devices to help solve network problems
Notes: Chapter Summary
There are many approaches to network troubleshooting including:
  Trial and error, solve by example, the replacement method, and step by step using the OSI model
Resources available to help troubleshoot include experience, the Web, and network documentation
There are several tools you can use to get information from your network and its devices to help solve network problems

## Slide 68: Chapter Summary
Some common troubleshooting situations are related to cable plant components, electrical power, and network and software upgrades
If your network is well documented, recovering from network disaster will be easier. Some of the tools to prevent disasters and expedite recovery include data backups, and system repair and recovery features in Windows
Notes: Chapter Summary
Some common troubleshooting situations are related to cable plant components, electrical power, and network and software upgrades
If your network is well documented, recovering from network disaster will be easier. Some of the tools to prevent disasters and expedite recovery include data backups, and system repair and recovery features in Windows